## Slide 1: IT 3123 Hardware and Software Concepts
Sequential Circuits and Memory
Notice: This session is being recorded.
Notes: Time: 0:51

## Slide 2: About ChatGPT and Others
The point of homework is to help you learn the material. Remember “rehearsal?”
If someone, or “some thing” else does the writing, you lose that rehearsal.
Absence of correct citation will cost you half the points.
Large Language Models are effectively lossy compression. Wrong answers are common and can cost you all the points.
Notes: Several of you turned in work for assignment 1 that showed unmistakable signs of being produced by ChatGPT or similar. That’s prohibited in this class
I hate marking homework. I’d rather do almost anything else. I assign homework to help you learn. Artificial responses do not accomplish that.

## Slide 3: Why do the Reading?
Are you reading the textbook?
You should… here’s why.
If you do the readings before class, you will be able to identify any concepts that are unclear to you.
And then you’ll have a chance to ask questions in class!
Besides, there might be questions on the exam.

## Slide 4: Combinational Circuits
A combinational circuit is a digital logic circuit the output of which is determined solely by its inputs.
Implication: combinational circuits have no memory.

## Slide 5: Combinational Circuit: Full Adder
After a brief gate delay, output changes to reflect the input.
Sum
Carry Out
Carry In
B
A

## Slide 6: Sequential Circuits
Sequential circuits have memory, or “maintain state.”
This is possible because of feedback; an output of the circuit is fed back to one of the inputs.
Truth tables are not applicable to sequential circuits.
Instead, a state table that has the output on both input and output sides is used.

## Slide 7: Reminder: the nor Gate
The output of nor is one or true only when both inputs are zero or false.
a
b
a+b
a​ | b​ | NOR
0​ | 0​ | 1​
0​ | 1​ | 0​
1​ | 0​ | 0​
1​ | 1​ | 0​

## Slide 8: Introducing the S-R Latch
Feedback
The S-R latch has two stable states. It is bistable.

## Slide 9: S-R Latch Sequence

## Slide 10: S-R Latch State Table
S | R | Q | Q'
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | X
1 | 1 | 1 | X
Notes: Q’ is read as “next Q.”

## Slide 11: Problems with the S-R Latch
You must have S and R; we’d really like to store bits.
S= 1 and R = 1 not allowed, but nothing prevents that.
We don’t really need Q.

## Slide 12: That 1-to-2 Decoder
Use a 1-to-2 decoder to drive R and S.
This fixes S=R=1, but now the output follows the input; no storage.
D
R
S
Q

## Slide 13: The D-Latch
S-R Latch
One to two decoder.
AND gates as Enable function.
D
Enable
D (data) is stored only when Enable is true. D is input to a decoder. Two and gates allow the signal from D to reach S or R when Enable is true.
Notes: Some books call this a D flip-flop. There are many other types of flip-flops. We won’t worry about them.

## Slide 14: The Tri-State Buffer
All the gates we have seen so far have an output that is either logic one or logic zero.
Sometimes we want no output at all, a “disconnected” state electrical engineers call high impedance or Hi-Z.
The tri-state buffer does that.
When Enable is logic true, input and output are connected.
When Enable is false, they are disconnected.
Input
Output
Enable

## Slide 15: Registers
This is a one-bit register.
The input bus is connected to D In all the time.
Data will only be sampled if both Write and Clock are logic 1.
Notes: The triangle symbol at “Enable” means this is an edge-triggered device. More on that in a moment.

## Slide 16: Register Output
The output is active all the time.
Output will reach the A or B Bus only if the corresponding tri-state buffer is enabled.
Both can be enabled at the same time.
Notes: The triangle symbol at “Enable” means this is an edge-triggered device. More on that in a moment.

## Slide 17: Two (or More) Bits in a Register
Notes: The input bus now has two lines. The first line is connected to the first, upper, latch. The second input line is connected to the second latch. The first latch’s A and B outputs are connected to the first lines of the A and B buses. The second latch’s A and B outputs are connected to the second lines of the A and B buses.
All the Write signals are connected together, as are all the clock lines, all the Enable A lines, and all the Enable B lines.
This can be extended to registers of many bits.

## Slide 18: Abstract Register
This is an n-bit, two output register.
Conceptually, it is n one-bit registers with n input bus lines and n A and B output bus lines.
The Clock signal is not shown (abstracted away.)
32
Notes: A fat arrow means multiple bits on a but. If it’s necessary to specify how many, we draw a diagonal line and label it with the number of bits.
Third click shows line and number making “Output A” a 32-bit bus.

## Slide 19: Think About Computation
Compute: A=A+B
A and B are in registers. Is there a problem?
Notes: The connection at the C-bus sends the sum of A+B back to A, but A is still enabled on the A-Bus and so is still input to the adder.

## Slide 20: The Computer’s Clock Signal
The clock for our hypothetical computer is asymmetric.
Registers are enabled on the falling edge.
Results are stored on the rising edge.
Adapted from Tanenbaum, Structured Computer Organization
Notes: Storage happens before changes to the destination registers can propagate back to the register inputs.

## Slide 21: Another Look at the Register
The triangle at input says this is edge-triggered.
Notes: An edge-triggered device captures input data on a change on the clock signal. Positive edge-triggered devices capture data on the rising edge of the coloc; negative edge-triggered devices capture on the falling edge.

## Slide 22: How to Make an Edge-Triggered Latch?
Check a digital logic book!
The essential idea is to use the very short gate delay through a gate to pass data from one latch to a second when the clock signal changes.
There are both rising-edge (positive) and falling-edge (negative) edge triggered devices.

## Slide 23: An Edge-Triggered Latch
Do not worry about this, OK! Just know that edge-triggered devices exist.
From Contemporary Logic Design Randy H. Katz

## Slide 24: Computation and the Clock
Falling edge: Registers A and B enabled on A- and B-buses.
The adder computes the sum, and after a time, the sum is stable on the C-bus.
Rising edge: The result from the C-bus is stored in A.

## Slide 25: A Nanosecond is This Long
Signals in computer systems travel at about 70% of the speed of light.
It takes non-zero time for a signal to travel between two points.
If gates are involved, they add gate delay.

## Slide 26: Why that Works
A and B are still enabled (connected) to the buses when the value on the C-bus changes.
However, the value is latched (stored) in A long before the change to A’s value can propagate through the A-bus and adder to the C-bus.
Notes: A and B are still enabled on the two buses; that won’t change until the control signals are set up for the next operation on the next falling edge. However, storing the value from the C-Bus in A happens very quickly on that rising edge. The value is latched long before the changed value of A can propagate through the combinational logic and be reflected on the C-Bus. So, the fact that the value on the C-Bus changes is not relevant because it happens too late to affect what is stored.

## Slide 27: Another Look at a Clock Cycle
Set up control signals.
Tolerance
Propa- gation on
A and B buses.
Propa- gation on C Bus
Computation through Adder/ALU
Adapted from Tanenbaum, Structured Computer Organization

## Slide 28: Out of the Weeds?
We will design a simple arithmetic/logic unit, then start looking at functionality and, at least mostly, leave gates behind.

## Slide 29: Questions