## Slide 1: IT 3123 Hardware and Software Concepts
Review and Questions Part 1
Notice: This session is being recorded.
Notes: Time: 1:08

## Slide 2: Abstraction
A mental model that removes unneeded complexity.
Different mental models can be at different levels of abstraction.
We will select different models (different levels of abstraction) for different purposes.
Abstraction and the construction of mental models is a superpower!
Notes: One of the tools that we use for developing mental models is this thing called abstraction.
Abstraction is removing unnecessary complexity and unnecessary and unneeded is bold and underlined because it is the key part of the definition.
Removes unnecessary complexity from the mental model.
So we can have different mental models at different levels of abstraction and we are going to do that. We will select mental models at different levels of abstraction as we work through the course this semester.

## Slide 3: One Model of Computing
This is the Input-Process-Output, or IPO, model; it is an example of abstraction.
Input
Output
Process
Storage
Notes: Here is one mental model of computing. This is the input process output or IPO model.
And there is nothing in there that looks like a computer very much. What we are focused on with this mental model is transformations.
Time cards go in, pay checks come out.
Test scores go in - course grades come out.
So we have an input, some sort of defined process, and a desired result.
And we can think about computing that way and all of the details about CPU and RAM and Gigahertz and all of that stuff is abstracted away. It is not important to this mental model. The mental model does include storage.

## Slide 4: Another Model
Notes: Here is another mental model, also an example of abstraction, but very different..
In this case it is a mental model of the physical parts of the computer. So I’ve got communications and keyboards and monitors and disks and printers and speakers.

## Slide 5: Computing in the 21st Century
Ubiquitous computers called “smart phones.”
Huge data centers with thousands of pizza-box size computers
Mainframe computers in about 2/3 of Fortune 100 businesses.
Supercomputers for modeling and other tasks.
Embedded computers.
And nearly all of them interconnected.
Notes: In the twenty-first century, digital computers are everywhere. You almost certainly have one with you now, although you may call it a “phone.” You are more likely to be reading this book on a digital device than on paper.
An electronic digital computer is a machine. It has mechanisms for receiving input of information, for processing and storing information, and for producing and communicating results. You will find computers in all kinds of specialized devices, but the computer itself is one of the most general-purpose machines ever devised. The more general a technology, the more and more varied the uses to which it will be put. We use computers for everything from preparing tax returns and processing them to landing airplanes, generating medical images, and displaying pictures of cats.

## Slide 6: Computer Components
Hardware
  Executes instructions
  Provides paths for input and output
  Provides temporary and long-term storage
Software
  Computer programs; instructions in machine language
Data
  Representation of facts, measurements, observations, in a form that can be used by the computer.
Notes: Every computer has hardware, software and data. You have to be really bold when you say “every.”
How about the computer that costs four cents to produce and goes inside one of those annoying greeting cards that does something when you open it up?
Hardware? Well yeah, there’s a little chip in there. Software? Yeah. Something happens to make that chip go. Data? Yeah. Sings “Happy Birthday to You.” So for the very simplest computer I can think of, we’ve got hardware, software, and data.
How about the Internal Revenue Service? A big computer somewhere in suburban Washington DC, out in McClean Virginia, somewhere maybe?
Hardware, software, data.
The hardware executes instructions and we will talk you know a fair amount of detail about what an instructions is and that mechanism for input and output and mechanism for both temporary and long term storage.
Software - that’s computer programs and by the time a program is actually being executed on computer it is in binary form in the language of the machine and we will talk about that in a certain amount of detail.
Data are representations of facts, measurements observations, information in a form that can be used by the computer and what we are going to find out is that form is binary numbers.

## Slide 7: Units of Memory
The smallest unit of storage is one bit; can hold only zero or one.
Bit: binary digit
Bits are organized into larger units.
  A byte (or octet) is eight bits.
  A word may be 16, 32, 64, or more bits, depending on the architecture of the computer.
  Computers (usually) perform arithmetic one word at a time; bigger words = faster computer.
Notes: The smallest unit of storage is one bit. “Bit” is a contraction of the words binary digit. We will talk about binary next time. A bit can hold only a zero or a one. A bit has only two possible values. We organize those bits into larger units. There’s no chance you have gotten this far as students in computing without hearing the word byte.
And “octet” is a synonym for byte; the two words mean the same thing.
That is a collection of eight bits - and you have talked about computers with 32 bit and 64 bit words. A computer “word” is the number of bits on which we do arithmetic so it could be eight or sixteen or 32 or 64 or even more. In general we perform arithmetic one word at a time... So bigger words in general imply faster computation. I can crunch more digits more bits in one operation if I have a 64 bit word than if I have a 32 bit word.

## Slide 8: Stored Program Concept
Stored program concept: The same memory can be used to hold instructions and data. (The program counter holds the address of the next instruction.)
Invented by John von Neumann and (probably) independently by others.
It’s software! Everything we do with software today depends upon the stored program concept.
Notes: The computer’s memory is also known as RAM or random access memory, main memory or primary storage. This is where programs and data live while the program is running.
So, as the slide says, memory holds instructions, and those instructions are in machine language, for programs that are running at the moment.
The stored program concept, something else invented by John von Neumann in the 1940s... There was this great ‘Aha!’ experience when von Neumann said you know, if I represent a program as a series of binary numbers, instead of as of as a collection of wires, I can store those binary numbers in the same memory that holds the data. And instead of having to rewire the computer when I have a new problem, all I have to do is load a new program into the computer’s memory.
This is obvious to us... But it was a great ‘Aha!’ about 1946 or 1947.
That program counter (which holds the address of the next instruction) is what keeps track of those instructions in main memory.

## Slide 9: Charles Babbage and Ada King
Charles Babbage built a difference engine for mechanical calculation.
Babbage attempted to build an analytical engine (mechanical computer). Important because it presented the idea of a general-purpose computing engine.
Augusta Ada King, Countess Lovelace developed fundamental concepts of programming.
Notes: Also in the 1800s, a Britisher by the name of Charles Babbage built a mechanical computer called the Difference Engine (because is used the method of finite differences for computation… look it up!) that was used to compute the navigation tables that British sailors used.
A navigational table like that is a star chart – it’s called an ephemeris - and Babbage was so successful with that he decided that is should be possible to build a general-purpose mechanical computer which he called the analytical engine.
He didn’t succeed but it is mostly because the technology for making sufficiently precise gears didn’t exist. There are modern copies of the analytical engine that work.
Augusta Ada King, Countess Lovelace, Lord Byron’s daughter, knew Babbage and developed some of the fundamental concepts of programming.

## Slide 10: The World War II Era
Alan Turing, father of Computer Science
  Code breaking for British military
  Colossus computer
1943-46: ENIAC (Mauchly, Eckert, University of Pennsylvania). First general-purpose electronic digital computer.
1945: Von Neumann architecture proposed. Still the standard for present day computers.
  Stored program concept: instructions and data
  Sequential execution and instruction cycle
  Use of binary numbers
Notes: Allen Turing invents computer science at Bletchley Park in England ... Something that he described as a place as ugly as its name.
And in 1945 John von Neumann was at the Los Alamos National Laboratory in New Mexico trying to solve the hydrodynamic equations of an H Bomb. The A Bomb was already taken care of by Oppenheimer and Feynman, right?
So von Neumann is trying to figure out the hydrodynamics of the hydrogen bomb with a pencil. And being one of the smartest people of the last century he quickly figured out that he could not do that. So - he hunted around for people who were working on electronic computing, went there, told them how to build a computer, and then disappeared back to Los Alamos and waited until they finished.
It was von Neumann who invented the stored program concept and invented the instruction cycle which we will talk about a little later in the semester, and the use of binary numbers with computing.

## Slide 11: Moore’s Law
1965: Gordon Moore, director of R&D at Fairchild Semiconductor wrote a magazine article.
Moore observed that the density of devices (transistors) on integrated circuit chips doubled about every two years.
The cost of a chip is proportional to the area.
If the density doubles, either the performance doubles or the cost is halved.
Notes: Moore’s Law isn’t really a physical law; it was an empirical observation that has been proven correct with minor differences for 60 years or more.

## Slide 12: The Internet and the World Wide Web
The Internet started with the Defense Advanced Research Projects Agency in 1966.
Beginning of NSFnet from the National Science Foundation in 1986.
World Wide Web invented by Berners-Lee, 1989.
Commercial Internet operation in 1995.
The Web and the Internet changed things fundamentally.

## Slide 13: Standards
Standards are created to assure compatibility of data formats and protocols
May be created by committee or may become a de facto standard through popular use
Allow computers and computer systems to interoperate
Languages, display standards, number formats, communication protocols, etc.
Notes: An important thing about modern computing is this idea of standards. What standards buy us is compatibility of either hardware or data or sometimes both.
Those standards might come from a committee like the American National Standards Institute, the International Standards organization, or the Institute for Electrical and electronic Engineers or a standard might be adopted from popular use - a De Facto standard rather than one that went through some sort of formal process.
It is the existence of standards that let computer systems inter-operate.
You go off and buy, I don’t know, it is a Gateway people still making computers? Nobody is saying anything so maybe not. You go off and buy somebody’s computer and you go over to microcenter and you buy a router made by somebody else and you expect to be able to plug them into one another and have them just work. That is the result of standardization.
In the 1960s if you bought a computer from IBM you bought everything else from IBM, too. Because nobody else’s equipment would work.
If you bought a computer from the Burroughs boys, you bought everything else from the Burroughs boys because nothing else would work with that Burroughs computer.
The development of standardization has moved us a huge way forward in computing.

## Slide 14: System Defined
A system is a collection of components…
linked together to perform specific functions, and
recognizable from the outside as a unit.
Everything outside the system is its environment, and
systems communicate with their environments through interfaces.
Notes: System: Here's the definition. A collection of components linked together to perform specific functions and recognizable from the outside as a unit. Everything outside the system is its environment. So, the self-driving car, that's the system. Everything outside is the environment. And systems communicate with the environment through interfaces.

## Slide 15: Numbers as Abstractions
Numbers can abstract physical quantities.
“Number systems” use sets of symbols to represent physical quantities. Cave dweller: llll ll Roman: Arabic-Indic: 7 (۷) Binary: 0111
Notes: The Roman number looks suspiciously like tally marks.

## Slide 16: Binary (Base 2) Numbers
2 digits: 0, 1
Powers of 2 example: 1 0 1 1 12
Notes: http://mathscitech.org/articles/zero-to-zero-power

## Slide 17: Converting Binary to to Decimal
Write down the powers of two below the digits, from right to left. Remember to start at 20 = 1 !
Write the decimal values of those powers of two.
Add up the powers of two for which the binary number bits are one.
1 0 1 1 1 2
24 23 22 21 20
16 8 4 2 1
16  4 2  1 = 2310
Notes: Write down the powers of two for each place, starting with two-to-the-zero power on the right.
Write down the decimal values of those powers of two.
Add up the decimal values for each position where the binary digit is a one,

## Slide 18: Powers of 2 to Memorize
24 = 16 For hexadecimal
28 = 256 Size of one octet
210 = 1,024 One “K”
220 = 1,048,576 One “meg”
230 = 1,073,741,824 One “gig”
232 = 4,294,967,296 Four gigs
232 is the most of anything (memory, disk, etc.) you can address (i.e. number) with a 32-bit word.

## Slide 19: IEC Prefixes for Powers of Two
Name | Abbr | Value
kibibyte | KiB | 210 = 1,024
mebibyte | MiB | 220 = 1,048,576
gibibyte | GiB | 230 = 1,073,741,824
tebibyte | TiB | 240 = 1,099,511,627,776
pebibyte | PiB | 250 = 1,125,899,906,842,624
exbibyte | EiB | 260 = 1,152,921,504,606,846,976
zebibyte | ZiB | 270 = 1,180,591,620,717,411,303,424
yobibyte | YiB | 280 = 1,208,925,819,614,629,174,706,176
Strictly speaking, these can refer to any units, not just bytes, e.g. one gibiword of memory.
Notes: The International Electrotechnical Commission has defined names for powers of two.
They are similar to kilo, mega, and giga, but contain the syllable bi for binary.

## Slide 20: Decimal to Binary
Notes: Divide the decimal number repeatedly by two. The remainders are the bits of the binary number. The remainder from the first division is the low order bit.

## Slide 21: How High Can We Count?
One bit: 0 or 1 0 to 1
Two bits: 00, 01, 10, 11 0 to 3
Three bits: 000, 001, 010, 011 0 to 7 100, 101, 110, 111
Four bits: 0000 to 1111 0 to 15
Five bits: 00000 to 11111 0 to 31
In general: n bits can count: 0 to 2n1 We can enumerate 2n things, starting at zero.
Notes: If we enumerate (number) things starting with zero, we can enumerate 2n items with an n-bit nuumber. The book starts with Chapter Zero to emphasize this. However, the largest unsigned number we can represent in n bits is 2n – 1 because one of the 2n items is zero.

## Slide 22: Binary Devices and Binary Numbers
A ten-element ring counter can count from zero to nine.
John von Neumann realized, and told his colleagues, that if the same ten binary elements were used to represent a binary number, one could count from zero to 1023.
We use binary devices for reliability.
We use binary numbers because it takes significantly fewer devices to represent a given value; use of binary numbers is economical because it maximizes the expressive power of binary devices.
Notes: http://en.wikipedia.org/wiki/Binary_number
The modern binary number system was discovered by Gottfried Leibniz in 1679 and appears in his article Explication de l'Arithmétique Binaire. However, systems related to binary numbers have appeared earlier in multiple cultures including ancient Egypt, China, and India. Leibniz was specifically inspired by the Chinese I Ching.

## Slide 23: Binary Addition
1 0 0 1 1 1 0 1 0 1 1 0 1 1 10 11




The first three of these are obvious. The fourth one is just 1+1=2
The last one is needed when you have a carry in. It is 1+1+1=3



## Slide 24: Finite-Precision Arithmetic
Finite Precision Arithmetic: Arithmetic on numbers for which the number of digits (precision) is fixed.
Computer operate on a fixed number of bits, 8, 16, 32, 64, or more, but always fixed!
Computer hardware works with finite-precision numbers.

## Slide 25: Two’s Complement
The leftmost bit (sign bit) represents a negative number times the power of two indicated by the position.
The remaining bits represent positive numbers added back to the negative value.
ai2i
i=0
n2

−an12n1 

## Slide 26: Complementing a Number
“Complementing” a number has the effect of multiplying by 1 or subtracting from zero.
Two steps:
  Complement (flip) each bit
  Add one to the result.
This is effectively subtracting the number to be complemented from zero.
The “trick” is that we subtract from minus one (all ones) then add one.

## Slide 27: A Shortcut
Copy the bits of the number, from the right, until you have copied a 1 bit.
Complement (flip) the remaining bits.
As taught by Dr. Hung and explained to me by someone who had taken the class.
0 0 0 1 0 1 1 1 1 1 1 0 1 0 0 1
1 1 1 0 1 0 0 0 + 1
1 1 1 0 1 0 0 1
0 0 0 1 1 0 1 0
1 1 1 0 0 1 1 0
1 1 1 0 0 1 0 1
+ 1 11 1 0 0 1 1 0
Notes: This works because adding one to a binary number is accomplished by flipping all 1s to 0s from the right until a 0 is reached, flip that to 1 and stop (essentially carrying the overflow of adding 1 to 1).
So one method flips only the bits to the left of the first one, while the other flips all bits, then flips the first 1 (now 0) and the bits to the right of it back.

## Slide 28: The Overflow Rule
Overflow: The condition that the result of an arithmetic operation is too large to fit in the space available.
If two numbers of opposite signs are added, overflow cannot occur.
If two numbers of the same sign are added and the result is of the opposite sign, overflow has occurred.
In other words, if I add two positive numbers and get a negative answer, something is wrong!
The “something is that overflow has occurred.
Notes: If you add two numbers of opposite sign, the magnitude of the result must be of smaller magnitude than either of the addends, so overflow cannot occur.
If you add two numbers of the same sign and get a result that is of the opposite sign, something is wrong! That “something” is that overflow has occurred.
In digital logic, The overflow condition is checked by comparing the carry in to the leftmost bit with the carry out from the leftmost bit. Recall that an XOR gate produces a one, or true, when the input bits are equal and a zero, or false when they’re different. There are two ways that can happen.
Case 1: If the carry in to the leftmost bit is zero, the only way the carry out can be one is if both A and B of the leftmost bit were one, i.e. both negative. The sum of 1+1 (plus zero for the carry in) will be zero with a carry out. The two operands were negative, but the leftmost bit of the result will be zero, or be positive, and overflow has occurred.
Case 2: If the carry in to the leftmost bit is one, the only way carry out can be zero is if both A and B of the leftmost bit were zero, i.e. positive. The sum of 0+0+1 will be one. The two operands were positive, but the carry out will be zero and leftmost bit of the result will be one, or negative, and overflow has occurred.

## Slide 29: Subtraction Rule
Form the two’s complement of the subtrahend.
Add it to the minuend

## Slide 30: Sign Extension Rule
Store a two’s complement number in a larger space by extending the sign bit on the left.
You can also remove bits from the left as long as removal doesn’t change the sign bit.

## Slide 31: Summary of Two’s Complement
Can represent positive and negative integers.
Asymmetric about zero.
Forming the two’s complement (How?)
Overflow rule (What is it?)
Subtraction rule.
Sign-extension rule.
Leftmost bit is the sign bit (1 is negative.)
Rightmost bit indicates even/odd (1 is odd.)

## Slide 32: Binary Fractions
We use a “binary point” to represent fractions. 0.12 = 2–1 = 1/2 0.012 = 2–2 = 1/4
Binary fractions are based on negative powers of 2.
Not all fractions can be represented exactly e.g. 1/3 and 1/10.

## Slide 33: Hexadecimal as Shorthand
0000 0 1000 8 0001 1 1001 9 0010 2 1010 A 0011 3 1011 B 0100 4 1100 C 0101 5 1101 D 0110 6 1110 E 0111 7 1111 F
Binary Hex
Binary Hex
Hexadecimal numbers are case-insensitive.
Be prepared to convert between binary and hex.

## Slide 34: Floating Point Numbers
Sign ( 1 bit)
Exponent ( 8 bits)
Significand ( 23 bits)
IEEE 754 32-bit Floating Point Format
The sign bit indicates the sign of the number
The exponent is also signed; +  1,  < 1
The signifocand holds the significant digits.
  n = (2c  s ) (positive if sign = 0, negative if 1)
Notes: The sign bit names this a signed-magnitude number
The exponent is stored as an excess 127 number, so it is signed.
Exponents are 1 to 254; effective range -126 to +127
zero and 255 are reserved.
The fraction has a “implicit one bit" because it is normalized.

## Slide 35: Range of Single Precision Floating-Point Numbers
Representable Negative Numbers
Representable Positive Numbers
Zero
Negative Overflow
Positive Overflow
Negative Underflow
Positive Underflow
<  2 +127
> 2 +127
< 2 126
>  2 126

## Slide 36: Summary of Floating Point
Key idea: Separate magnitude from precision
We trade precision for range (no free lunch)
Normalize for best precision
Floating point numbers are approximate!
Rounding errors can accumulate.
Floating-point arithmetic is finite-precision arithmetic; the associative and distributive laws do not apply near the boundaries.

## Slide 37: Graphemes and Glyphs
A grapheme is the smallest functional unit of a writing system:
  Latin small A is a grapheme.
  Greek small alpha is a different grapheme.
Graphemes are expressed as glyphs.
  Latin small A: a or a or a.
  Greek small alpha: α
Same grapheme, different glyphs.
Similar glyph, different grapheme.
Notes: In linguistics, a grapheme is the smallest functional unit of a writing system https://en.wikipedia.org/wiki/Grapheme
Graphemes are expressed as glyphs.
In typography, a glyph is an elemental symbol within an agreed set of symbols, intended to represent a readable character for the purposes of writing and thereby expressing thoughts, ideas and concepts. As such, glyphs are considered to be unique marks that collectively add up to the spelling of a word, or otherwise contribute to a specific meaning of what is written, with that meaning dependent on cultural and social usage. https://en.wikipedia.org/wiki/Glyph
The Greek small alpha looks like a Latin small A without hook but is a different grapheme.

## Slide 38: The Number One and the Symbol 1
The binary number one (in 8 bits) is: 0000 0001
The ASCII code for the grapheme “1” is 011 0001
They are not the same!
“One” is an integer “1” is a code for a symbol, or grapheme.

## Slide 39: Unicode
Idea: A single coding scheme that represents all the possible characters in all the world’s languages. (Over 200,000 symbols are required.)
And be able to represent dead languages… things like cuneiform (Sumero-Akkadian) and medieval languages, and… and… everything!
That would take about 18 bits per character; a distinctly odd number for byte-oriented computers.
Compromise was needed!

## Slide 40: Unicode and Transformation Formats
Unicode maps numbers (code points) to graphemes.
The first 128 code points correspond to U.S. ASCII.
The first 256 code points correspond to ISO-8859.
A Unicode Transformation Format describes how those numbers will be represented in computer storage.

## Slide 41: Implementing Unicode: UTF-8
Idea: I can encode ASCII (the first 128 characters of Unicode) in seven bits.
In an 8-bit byte, I can use that extra bit to say, “more is coming” and get a variable length code with “leading bytes” and “continuation bytes.”
Bits | Last code point | Leading Byte | Byte 2 | Byte 3 | Byte 4
7 | U+007F | 0xxxxxxx |  |  | 
11 | U+07FF | 110xxxxx | 10xxxxxx |  | 
16 | U+FFFF | 1110xxxx | 10xxxxxx | 10xxxxxx | 
21 | U+10FFFF | 11110xxx | 10xxxxxx | 10xxxxxx | 10xxxxxx
Notes: UTF-* is Unicode Transformation Format, 8 bit.
UTF-8 originally allowed for 6 bytes and 31 bits; restricted in 2003 to match the 16 planes of Unicode.

## Slide 42: How Does The Computer Know?
Using ASCII, the letter A is 01000001
Also, 010000012 = 6510
How does the computer know whether it’s an A or a 65?
Context! The programmer must keep track of whether the binary data represent letters, numbers, or something else.

## Slide 43: Encoding Pictures
Each dot is called a Picture Element, or pixel.
The number of pixels per inch (or millimeter) determines the resolution or fineness of the picture. More is better.
The number of bits per pixel determines the color depth; again, more is better.
Each pixel is one or more binary numbers.
Notes: Pixels are sometimes called pels.

## Slide 44: Additive Colors – The RGB Model
Computer displays emit light; we use the concept of additive colors to make many colors from the three primary colors, red, green and blue.

## Slide 45: Subtractive Colors – CMYK Model
Printing depends on reflected light. Cyan reflects blue and green, absorbs red. Magenta reflects red and blue, absorbs green. Yellow reflects red and green, absorbs blue.
Black is needed because CMY together are sort-of muddy brown.
Notes: A fourth ink, black, is necessary because cyan, magenta, and yellow together make a sort-of muddy brown.

## Slide 46: Raster Images
GIF, JPEG, and PNG are raster image formats, also called bitmap images.
They are composed of rows of pixels.
There are other bitmap formats.

## Slide 47: Vector Images
Geometric objects can be described mathematically.
Circle: Center, radius, line width, and color.
Much more compact storage than a bitmap.
Needs more computation.
Converted to bitmap for display.
SVG is a common vector format.

## Slide 48: Sounds
Sound is inherently analog (continuous)
Two dimensions
  Amplitude (loudness)
  Frequency (pitch)
Each can vary independently of the other
Amplitude
Frequency

## Slide 49: Encoding Sounds
Sample: 255 (large amplitude value)
Sample: -32 (small amplitude value)
http://musikality.net/wp-content/uploads/2009/01/quantised_waveform.png
Neither samples nor interpolation between samples is exact. The samples are integers.

## Slide 50: How Many Samples?
Nyquist’s sampling theorem: Sample at twice the maximum frequency you want to reproduce. (This is a theoretical minimum sampling rate.)
Frequencies are expressed in Hertz (cycles per second.) A = 440 Hz.
To reproduce 20,000 Hz, sample at 40,000 Hz. or more.
Notes: Nyquist’s sampling theorem is also called the Nyquist–Shannon sampling theorem.
The 440 A is A above middle C.

## Slide 51: Switching Algebra
A special case of Boolean algebra.
Variables can only be one of two values, zero or one.
Zero and one can represent false and true, respectively.
So, an algebra over sets of binary digits.
Often called “Boolean algebra” by those involved in computing.

## Slide 52: Truth Tables
A more visual way to represent Boolean functions. Developed from the work of Jan Łukasiewicz.
Here is f(a,b) = a•b, the AND function. Note that if you consider a and b as digits of a binary number, the values are written in ascending order.
a | b | f(a,b)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: You are responsible for the truth tables of all the functions we studied.

## Slide 53: The “Characteristic Number”
If the left (input) side of a truth table is always written in ascending order, we don’t really need to show it.
You can think of the result of a function as a number that characterizes the function. The and function has characteristic number 0001.
a | b | f(a,b)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: You should be able to write the truth tables of all functions we’ve studied, not just AND.

## Slide 54: Abstraction
We use special symbols to represent the electronic circuits that make up digital logic gates.
NAND
NOR
Know the truth tables, too!

## Slide 55: Functional Completeness
NAND and NOR are functionally complete.
Functionally complete: Any digital logic function can be computed using only one type of functionally complete gate.
Any function can be computed using only NAND gates.
Any function can be computed using only NOR gates.

## Slide 56: Logic Diagrams
Logic diagrams are abstractions of logic circuits.
Gate symbols represent corresponding gates.
Lines represent connections: wires, traces on a printed circuit board, or conductors within a chip.
Power and ground connections are omitted.
Connections are shown with a heavy dot.
No dot means no connection.

## Slide 57: Combinational Circuits
A combinational circuit is a digital logic circuit the output of which is determines solely by its inputs.
Implication: combinational circuits have no memory.

## Slide 58: Full Adder: Two Half Adders
Two Half-Adders and an OR gate
Notes: Another way of thinking about the full adder is that it’s two half-adders. One computes the sum of the inputs, and the other adds carry-in to the sum. The OR gate combines the two carry out possibilities.

## Slide 59: Abstraction
Full Adder
A
B
Ci
Co
S

## Slide 60: About Digital Logic Gates
The output of a digital logic gate depends only upon its inputs; changing the inputs changes the output.
The transistors in a digital logic gate take a few nanoseconds (billionths of a second) to switch from on to off or vice-versa.
The gate delay of a digital logic gate is the time for a change in inputs to be reflected in a new output.
Notes: There is also a propagation delay, the time for the output of one gate to reach the input of the next one. Propagation occurs at 50 to 99% of the speed of light.

## Slide 61: Digital Logic Building Blocks
Decoder: n bits of input, 2n output lines, exactly one of which is high depending on the input.
Encoder: 2n input lines exactly one of which is high, n outputs that form a binary number showing which input line is high.
Multiplexor: An n-bit control signal that selects one of 2n inputs to connect to the output.
Shifters: Shift a group of bits left or right, implementing multiplication or division by 2.
Others…

## Slide 62: A Word About Chips
Small-scale integration packages gates.
Medium-scale integration packages simple functions.
Large-scale and Very large-scale integration package complex functions or complete systems.
Notes: In this case, “package” is a verb.

## Slide 63: Sequential Circuits
Sequential circuits have memory, or “maintain state.”
This is possible because of feedback; an output of the circuit is fed back to one of the inputs.
Truth tables are not applicable to sequential circuits.
Instead, a state table that has the output on both input and output sides is used.

## Slide 64: S-R Latch State Table
S | R | Q | Q'
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | X
1 | 1 | 1 | X
Notes: Q’ is read as “next Q.”

## Slide 65: The D-Latch
S-R Latch
One to two decoder.
AND gates as Enable function.
D
Enable
D (data) is stored only when Enable is true. D is input to a decoder. Two and gates allow the signal from D to reach S or R when Enable is true.
Notes: Some books call this a D flip-flop. There are many other types of flip-flops. We won’t worry about them.

## Slide 66: The Tri-State Buffer
All the gates we have seen so far have an output that is either logic one or logic zero.
Sometimes we want no output at all, a “disconnected” state electrical engineers call high impedance or Hi-Z.
The tri-state buffer does that.
When Enable is logic true, input and output are connected.
When Enable is false, they are disconnected.
Input
Output
Enable

## Slide 67: Registers
This is a one-bit register.
The input bus is connected to D In all the time.
Data will only be sampled if both Write and Clock are logic 1.
Notes: The triangle symbol at “Enable” means this is an edge-triggered device. More on that in a moment.

## Slide 68: Register Output
The output is active all the time.
Output will reach the A or B Bus only if the corresponding tri-state buffer is enabled.
Both can be enabled at the same time.
Notes: The triangle symbol at “Enable” means this is an edge-triggered device. More on that in a moment.

## Slide 69: Two (or More) Bits in a Register
Notes: The input bus now has two lines. The first line is connected to the first, upper, latch. The second input line is connected to the second latch. The first latch’s A and B outputs are connected to the first lines of the A and B buses. The second latch’s A and B outputs are connected to the second lines of the A and B buses.
All the Write signals are connected together, as are all the clock lines, all the Enable A lines, and all the Enable B lines.
This can be extended to registers of many bits.

## Slide 70: Abstract Register
This is an n-bit, two output register.
Conceptually, it is n one-bit registers with n input bus lines and n A and B output bus lines.
The Clock signal is not shown (abstracted away.)
32
Notes: A fat arrow means multiple bits on a but. If it’s necessary to specify how many, we draw a diagonal line and label it with the number of bits.
Third click shows line and number making “Output A” a 32-bit bus.

## Slide 71: Think About Computation
Compute: A=A+B
A and B are in registers. Is there a problem?
Notes: The connection at the C-bus sends the sum of A+B back to A, but A is still enabled on the A-Bus and so is still input to the adder.

## Slide 72: The Clock Cycle
Set up control signals.
Tolerance
Propa- gation on
A and B buses.
Propa- gation on C Bus
Computation through Adder/ALU
Adapted from Tanenbaum, Structured Computer Organization

## Slide 73: An Edge-Triggered Latch
Do not worry about this, OK! Just know that edge-triggered devices exist.
From Contemporary Logic Design Randy H. Katz

## Slide 74: Computation and the Clock
Falling edge: Registers A and B enabled on A- and B-buses.
The adder computes the sum, and after a time, the sum is stable on the C-bus.
Rising edge: The result from the C-bus is stored in A.

## Slide 75: Questions