## Slide 1: IT 3123 Hardware and Software Concepts
Let’s Build a Computer
Notice: This session is being recorded.
Notes: We're finally ready to use what we've learned to design a simple computer. Although it's simple, it is powerful enough to run real programs and illustrates how the pieces of the von Neumann architecture fit together.

## Slide 2: Problems with LMC
LMC is a decimal computer, but real computers are binary.
There is a certain amount of “magic” in the actions of the Little Martian, but no magic in real computers.
The available simulators do not show the fetch / decode / execute cycle clearly.
So… we’ll do something else! A computer called TBC.
Notes: The fact that real computers are binary is important because the use of binary representation has a powerful effect on how data are represented. It also explains why there are powers of two everywhere we look

## Slide 3: Reminder: Registers
Small, fast storage within the CPU.
From “a few” to a few hundred.
One input, one or a few outputs.
Conceptually, the right number of latches.
From “a few” to 64 or more bits wide.
“Fat arrows” indicate multi-bit paths.

## Slide 4: Computers Have Registers
The Little Martian could remember things; in a real computer, registers do that.
Arithmetic results: The accumulator or general registers, also called data registers.
The memory location to read or write: The memory address register.
The data transferred to or from memory: The memory data register, also called the memory buffer register.
Address of the next instruction: The program counter.
The current instruction read from memory: The instruction register.

## Slide 5: General Registers
General registers, also called data registers, are registers available to the programmer.
Usually receive the results of operations like arithmetic.
If there is only one such register, it is called an accumulator.
Notes: The one data register in the von Neumann architecture was originally called an accumulator because it accumulated the results of arithmetic operations.

## Slide 6: Memory Registers
The memory address register holds an address in memory:
  From which to read data
  To which to write data
The memory data register holds data or instruction words:
  Read from memory
  To be written to memory

## Slide 7: Program Counter
Holds the address of the next instruction
Updated shortly after an instruction is fetched
Can be changed (by the CPU) to implement branching.

## Slide 8: Instruction Register
Holds the instruction fetched from the memory location pointed by the Program Counter
The “Decode” phase examines the contents of the instruction register to decide what operation to perform
The instruction was something the Little Martian remembered; a real computer uses the Instruction Register

## Slide 9: About LMC’s Calculator
Does three things:
  Receive data from the Little Martian
  Performs arithmetic operations
  Holds the result of arithmetic operations
Two separate components in a real computer:
  The arithmetic/logic unit performs arithmetic and logical operations.
  Data registers or accumulator (if there’s only one) receive the results of arithmetic and logical operations.

## Slide 10: The Arithmetic / Logic Unit
LMC performs addition and subtraction with the calculator.
We must also be able to copy data into the accumulator, i.e. enter numbers.
To do what LMC does, we need these functions:
  Add
  Subtract
  Copy
  Increment (add one)
It is also useful to generate constants like zero and one.

## Slide 11: Making an ALU: Start With a Full Adder
This is the same circuit we saw in the study of digital logic, slightly rearranged.
It adds two bits, a and b, and a carry-in to produce a sum (output) and carry-out.
Notes: “Rearranged:” It’s still exactly the same circuit in terms of gates, wiring, and logical flow; the positions of the gates have been moved slightly to make adding to the circuit easier.

## Slide 12: AND as an “Enable” Control
The and gate can be used as an “enable” gate to control whether a signal passes through it or not.
When Ena (enable) is zero (false), the result f is zero.
When Ena is one (true), the result f is equal to a.
Ena | A | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a Ena
f

## Slide 13: Provide “Enable-B” Input
If Enable b is true, the value of b is passed to the full adder.
If not, the b input of the adder is zero.
This will let us copy a from input to output without addition by “adding” zero.
b Ena b

## Slide 14: XOR as Controlled Inverter
The xor gate can be used as an “invert or not” gate.
When Inv is zero (false), a is passed through unchanged.
When Inv is one (true), a is inverted i.e. the result is .
Inv | A | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a Inv
f

## Slide 15: Provide Control Inputs for a
Two new control inputs:
Enable a passes the a value to the XOR gate that’s a controlled inverter, or sends zero.
Invert a complements (inverts) the a input; this will be used for subtraction.
a Ena a Inv a

## Slide 16: A One Bit (Bit-Slice) ALU
A full adder with three data inputs: a, b, ci
Three control inputs:
  Enable a
  Invert a
  Enable b
Output and co

## Slide 17: Make the Full ALU from Bit Slices
This is the same principle as the ripple-carry adder. We can have more than four bits.
A new control input, Inc (increment), can place a zero or one on the rightmost carry in.
Notes: Notice that Invert A, Enable A, and Enable B are connected to every bit slice. In a real design, we would have to worry about the “fanout,” the ability of one signal to drive many inputs.

## Slide 18: Detecting Overflow
Overflow is an unrecoverable error that causes a “program check.” XOR is used as “not equal.”
Notes: The check for overflow compares the carry-in to the leftmost bit to the carry-out. If they are not equal, overflow has occurred. Explanation on next slide.

## Slide 19: About Detecting Overflow
Remember the overflow rule? Changed sign means overflow.
The circuit on the previous slide XORs carry in and carry out of the leftmost bit.
Case 1: 0 carried in and 1 carried out… the inputs to the leftmost bit must both be 1 or negative, but the result will be positive.
Case 2: 1 carried in and 0 carried out… the inputs to the leftmost bit must both be 0 or non-negative, but the result will be negative.
Notes: The overflow rule for two’s complement addition is: overflow has occurred if two numbers of the same sign are added and the result is of the opposite sign.
Consider the inputs A and B to the leftmost bit, or sign bit.
xor computes a “not equal” function; it generates a one, or true, when the two inputs to the XOR are not equal.
The xor gate on the previous slide produces a one, or true, when the carry into the leftmost bit is not equal to the carry out.
When does that happen? There are two cases.
Case 1: If the carry into the leftmost bit is zero, the only way the carry out can be one is if both A and B of the leftmost bit were one, i.e. both negative. The sum of 1+1 (plus zero for the carry in) will be zero with a carry out. The two operands were negative, but the leftmost bit of the result will be zero, or be positive, and overflow has occurred.
Case 2: If the carry into the leftmost bit is one, the only way carry out can be zero is if both A and B of the leftmost bit were zero, i.e. positive. The sum of 0+0+1 will be one. The two operands were positive, but the leftmost bit of the result will be one, or negative, and overflow has occurred.

## Slide 20: Detecting Positive
If the leftmost bit is a zero, indicating a positive two’s complement number, the NOT gate will produce a one.
Notes: The check for Positive just inverts the sign bit. If the sign bit is one (negative) the P output will be zero. If the sign bit is zero (positive) the P output will be 1. Note that the value zero is considered positive when done this way.

## Slide 21: Detecting Zero
A 4-input NOR gate produces a one when all four output bits are zero.
Notes: The zero detector is a NOR gate with one input for each bit. In the example, it’s a four-input NOR. For a 12-bit computer, it would be a 12-input NOR. If all of the output bits are zero, Z will be one.

## Slide 22: Using Overflow, Positive, and Zero
Overflow causes a “program check.” P and Z are stored in a latch whenever a value is stored in Acc, the Accumulator.
Notes: In this simple case, overflow is an unrecoverable error. The P and Z values are stored in a latch whenever a value is stored in the accumulator, so the P/Z latch always reflects the value in the accumulator.

## Slide 23: What Can We Do with this ALU?
Much more complex ALUs are possible. This one does everything we need using only eight gates per bit! (Plus a few for V, P, Z.)
Inc
Ena
B
Inv
A
Ena
A
·
·
Add (A + B)
·
·
·
·
Subtract (B
–
A)
·
Copy A
·
·
Increment A
Constant zero
·
Constant one
·
Constant minus one
Notes: What can we do with this ALU?
If Ena A and Ena B are true and Inv A and Inc are false, the circuit functions as a full adder, adding A, B, and Ci to produce the sum at Out and the carry out at Co.
The subtract function applies the subtraction rule for two’s complement numbers, namely take the two’s complement of the subtrahend and add it to the minuend. The ALU forms the two’s complement of A by inverting the A bits using Inv A and adding one by setting Inc. The adder completes the operation.
The copy A function actually computes A+0 by turning off Ena B. A copy B function, not shown in the table, could be implemented similarly.
The Increment A operation enables A and adds one with the Inc control. An increment B function could be implemented similarly.
If Ena A, Ena B, Inv A, and Inc are false, the adder computes 0+0 and emits a constant zero. If Inc is true and Ena A and Ena B are false, the adder computes 1+0, and emits a constant one.
A constant minus one is produced when Ena A and Ena B are both false and Inv A is true. Having Ena A false sends logic zero to the xor gate that serves as a controlled inverter. Inv A changes the zero to a one. Because Ena B is false, the adder computes 1+0 for each position, and produces a string of all ones at the outputs. Recall that a string of all ones is a two’s complement minus one.

## Slide 24: Buses
Bus: just a bunch of conductors carrying related signals.
The buses in this diagram carry data only.
Other possibilities are, addresses, control and status.
Some buses, like USB, carry power and ground.

## Slide 25: Abstraction: The ALU Symbol
C Bus
A Bus
B Bus
Control
P, Z, V
Notes: The truncated V is an abstract expression for an ALU. Once we understand how out ALU is designed, we can abstract away the design details. Remember that “fat arrows” represent multi-bit paths.

## Slide 26: Start with an ALU
Notes: Let’s build a small CPU. We’ll start with an ALU like the one just designed.

## Slide 27: Add a Register and Buses
Notes: Add a register, the accumulator, labeled Acc.

## Slide 28: Add a Control Unit to Generate Signals to the ALU
Notes: We add a control unit to generate the control signals needed by the ALU.

## Slide 29: The Control Unit Also Generates Signals for the Registers
Notes: The control unit also generates signals for the registers. The closed-head arrow labeled Write signals the accumulator to load itself from the C Bus on the rising edge of the clock if the signal is asserted. The closed head means this signal depends on the clock.
The open-headed arrows, Out A and Out B, if asserted, signal the accumulator to place its contents on the A bus or B bus, respectively. These signals do not depend on the clock; the contents of the accumulator will appear on the selected bus for as long as the signal is asserted.

## Slide 30: Add More Registers
Notes: We add two more registers, the program counter, labeled PC, and the instruction register, IR. The “disembodied arrows” connecting to the registers and memory all come from the control unit. Arrows with closed heads indicate loading the register from C at the end of the clock cycle. The open head arrows indicate sending the register contents into the A or B bus. Only the accumulator can connect to the B bus; the others can send their contents only to the A bus. At most one register can be selected for each bus in one clock cycle. As before closed head arrows mean that signal depends on the clock to be effective; open head arrows mean a signal is effective whenever it is asserted.

## Slide 31: Connect to Memory
To and from main memory
Notes: Connecting to memory needs two more registers, the memory address register and the memory data register. The memory address register can only accept address information from the C bus. The memory data register can send data to the A bus or accept data from the C bus.

## Slide 32: Save the P and Z Flags
To and from main memory
Notes: We add one more register, the P-Z latch. This one stores only two bits, the P and Z flags from the ALU. The closed head arrow means P and Z are stored only on the rising edge of the clock. The write signal to the P-Z latch is the same as that to the accumulator. The P and Z bits are saved any time the accumulator is loaded, and so reflect the contents of the accumulator.

## Slide 33: Data Path: The ALU and Registers
To and from main memory
Notes: The buses are also part of the datapath. The control unit is not part of the data path.

## Slide 34: Data Path Timing (The Clock)
Set up control signals.
Tolerance
Propa- gation on
A and B buses.
Propa- gation on C Bus
Computation through ALU
Adapted from Tanenbaum, Structured Computer Organization

## Slide 35: Control Unit Design
Hardwired: The necessary control signals are generated using digital logic gates. Fastest and most expensive.
Microprogrammed: The necessary control signals are generated from read-only memory using a simple control circuit. Less expensive, but slower.
Hybrid: Frequently used instructions are hardwired; the rest are microprogrammed.
Notes: Hardwired control units generate the necessary control signals using digital logic gates. Hardwired control units are fast, but also expensive because of the number of gates needed.
Microprogrammed control units use a read-only memory to generate the bits of the control signals. Each word in the ROM must have enough bits to generate all the control signals, and there must be one word for each datapath cycle. Very simple digital logic reads the ROM. Microprogrammed control units as less expensive because they need fewer gates, but also slower because a ROM access is needed for each datapath cycle. In addition to lower cost, microprogrammed control units have the advantage that the microprogram can potentially be changed.
Some modern CPUs use hybrid control units. The frequently-used instructions are implemented using hardwired control, and the less frequently-used instructions are microprogrammed.

## Slide 36: The TBC Control Unit: Input
The Instruction Register (IR) holds the operation code and operand address.
The control unit receives:
  4 bits of operation code from the instruction register.
  The P and Z flags from the ALU, stored in a latch.
  For hardwired control, three bits of “cycle count.” (Where are we in the instruction?)

## Slide 37: The TBC Control Unit: Output
The control unit generates:
  4 bits of ALU control input (EnaA, InvA, EnaB, Inc).
  Read, write, and presence-detect signals for memory.
  Output and write signals for the registers.
  In this case, a total of 17 bits.
Notes: The Op Code, Jump, and Next Address bits are used in the microprogrammed control unit. There are details in Appendix B of the textbook. The “not used” bits make a total of 32 bits, a standard size for read-only memories.

## Slide 38: The Instruction Cycle
The von Neumann Instruction Cycle
Fetch: Get an instruction from the memory location pointed by the program counter and advance the program counter.
Decode: Determine what operation code is present, and what data to use.
Execute: Perform the commanded operation.

## Slide 39: Register Transfer Language
The basic operation of the execute part of the instruction cycle: send the contents of one or two registers through the ALU.
The result is stored in a register, possibly the same as one of the sending registers.
Data are transformed according to the command (add, subtract, etc.) given the ALU.
The “copy” command can move data without changing it.
Register operations are described with RTL

## Slide 40: The Instruction Cycle: STORE
Fetch
Decode
Execute
MAR ← PC (read memory)
Determine next operation from IR
MDR ← A
PC ← PC+1
IR ← MDR
MAR ← IR[addr] (write memory)
Notes: Each rectangle represents one datapath cycle. The first three cycles are the same for every instruction. They fetch the instruction from memory. In the first datapath cycle, the program counter is copied to the memory address register. In parentheses is “read memory.” The control unit generates a read signal to the memory system.
In the next datapath cycle, the program counter is incremented. This happens while the memory read is completing.
By the third cycle, the fetched instruction is in the memory data register. It is copied to the instruction register, and the fetch part of the instruction cycle is complete.
The control unit is fast enough to decode the instruction before the next falling edge of the clock, and so does not require a datapath cycle.
In the execute phase, first the accumulator is copied to the memory data register. In the last datapath cycle, the square brackets around ADDR mean only the address portion of the instruction register are copied to the memory address register. Memory is commanded to write, and the instruction ends.

## Slide 41: Register Transfer Example: MAR←PC
Copy
Out A
Write
Control
P/Z Latch
Notes: How does that work on the datapath? Let’s look at an example, copying the program counter to the memory address register.
On the falling edge of the clock signal, the ALU is commanded to copy, the program counter register is enabled on the A bus, and a write signal is asserted on the MAR. During the clock’s low period, data travel from the PC through the ALU to the MAR. The rising edge of the clock signals the MAR to store with contents from the C bus.

## Slide 42: The Datapath Computes PC ← PC+1
Out A
Notes: Here’s another example, incrementing the program counter.
To increment the program counter, on the falling edge of the clock the PC register is enabled on the A bus and the ALU is commanded to increment. The addition occurs and the incremented program counter value appears on the C bus. On the rising edge of the clock, the incremented value on the C bus is stored in the PC register.

## Slide 43: Introducing TBC!
It’s a “Tiny Binary Computer.”
Starting with a full adder, we built a CPU…
That will execute the LMC instruction set.
It’s a binary computer, like real ones.
There is no “Little Martian” and no magic; it’s all digital logic, with a bit of ROM.
(I-O remains a bit mysterious for the moment.)

## Slide 44: It’s a Twelve-Bit Computer
Four bits of op code (So, 16 combinations.)
Eight bits of address (256 words of memory, but only 128 installed.)
Integer range from –2,048 to +2,047
It will run LMC programs (if reassembled)
Data word
Two’s Complement Integer
Instruction word
Op Code
Address
0
11
8 7

## Slide 45: The TBC Simulator

## Slide 46: Using the TBC Simulator
It’s on the Web: https://computingconcepts.net/tbc/
Your programs are stored in the browser’s memory.
That means you can’t easily switch computers or even switch browsers.
You can copy information out of TBC’s source code pane and save it with Notepad or another editor.

## Slide 47: Preparing Programs
Type your source program here. Save it in the browser.
The assembled (translated) program is displayed here when you click the “Assemble” button.

## Slide 48: The Assembled Program
Line Addr Object Source Code
Code
1. 00 901 in
2. 01 30a sto first
3. 02 901 in
4. 03 30b sto second
5. // The second number
6. 04 20a sub first
7. 05 808 brp print
8. 06 50a lda first
9. 07 20b sub second
10. 08 902 print out
11. 09 000 hlt
12. 0a 000 first dat 0x00
13. 0b second dat

## Slide 49: The Program in Memory

## Slide 50: Running Programs
The “Control Panel” lets you load and run assembled programs.
Output is on the screen.
You can change the clock speed.
You can step programs one instruction at a time.

## Slide 51: “As close as we can get…”
TBC is very close to a real computer design.
  There is no magic
  There is very little hand-waving; only in how programs are loaded. (We didn’t discuss the control unit much, but it’s not magic!)
In theory, you could go to the digital logic lab and build TBC.
We’ve left out power supplies, clock generator, and some details of bus design. For this course, those are “abstract details.”

## Slide 52: Is TBC Realistic?
The first widely successful mini-computer was the DEC PDP-8. It used 12-bit words.
It had an instruction set of eight instructions (smaller than TBC’s).
The PDP-8 could run a complete multi-user operating system.

## Slide 53: The PDP-8
Notes: One version of the PDP-8 was desktop size, about the size of a bread box.

## Slide 54: Something to Think About
The PDP-8 had an add instruction, but no subtract instruction.
How do you think subtraction was performed?
Hint: the mnemonic for the add instruction was TAD for “two’s complement add.”

## Slide 55: Using TBC
To use TBC, the programmer must understand the TCB instruction set…
And also one pseudo-instruction.
For this course, there’s a TBC simulator. You’ll use that to develop programs.
Let’s look at the instruction set and an example program.

## Slide 56: The LMC/TBC Instruction Set
Mnemonic Op Code Meaning
HLT 0xx Halt
ADD 1xx Add
SUB 2xx Subtract
STO 3xx Store
LDA 5xx Load
BR 6xx Branch
BRZ 7xx Branch Zero
BRP 8xx Branch Positive
IN 901 Input
OUT 902 Output
Notes: HLT ends the program
ADD adds the data at the memory address given to the contents of the accumulator
SUB subtracts the data at the memory address given from the contents of the accumulator.
STO stores the accumulator contents at the memory address given.
LDA loads the data at the memory address given into the accumulator. The previous contents of the accumulator are lost.
BR takes an unconditional branch to the address in the instruction
BRZ branches to the address given only if the Z flag is set, that is, if the accumulator contains a zero.
BRP branches to the address given only if the P flag is set, that is, if the accumulator contains a positive number or zero.
IN reads one 12-bit word from outside and places it in the accumulator. The previous contents of the accumulator are lost.
OUT writes the contents of the accumulator to the screen. The contents of the accumulator are unchanged.
Complete semantics of the TBC instruction set are in Appendix A of the textbook.

## Slide 57: A Pseudo-Instruction
The LMC/TBC assembler recognizes the DAT (for “data”) mnemonic.
DAT is not an instruction; it is a command to the assembler to reserve one location for data.
Such assembler commands are called pseudo-instructions
Could also be used to reserve and initialize data, e.g. DAT 20

## Slide 58: A Previous Semester’s Homework
Part 4: Design a program that displays the even numbers counting downward from 20 to zero using the LMC / TBC instruction set and looping. The program must halt after displaying zero. Write and turn in the pseudo-code for your solution and your final program.

## Slide 59: The Expected Result
20
18
16
14
12
10
8
6
4
2
0

## Slide 60: Elements of the Problem
Start at 20
Count down
Even numbers only
Use a loop
Stop after displaying zero

## Slide 61: Pseudo-Code for Data
Number? 20 to start
Value to subtract? 2

## Slide 62: Pseudo-Code for Instructions
get starting number
print print the current value
was it zero?
if yes, stop
subtract 2
go to print
Remember, data goes at the end!

## Slide 63: One Way to Approach This
lda number print out brz done sub two br print done hlt
number dat 20
two dat 2

## Slide 64: Assembling the Program (Error!)
Notes: “two” was misspelled the first time. The error message was where “two” was used, not where we tried to define it.

## Slide 65: Assembling the Program

## Slide 66: The Object Listing Area

## Slide 67: Run the Program

## Slide 68: TLC’s Memory at the End

## Slide 69: What If…
What if we were asked to stop at a number other than zero?
We’d have to:
  Save the current number to memory
  Subtract the “stop limit” from it
  Branch on zero (numbers were equal)
  If not zero, restore the current number from memory

## Slide 70: More Help
There’s an example of using TBC here:
https://mediaspace.kennesaw.edu/media/Using%20the%20Tiny%20Binary%20Computer%20Simulator/1_oqoi1yg8

## Slide 71: Three Important Facts
Grace Murray Hopper helped with the invention of compilers so that we wouldn’t have to program in assembly language.
A high-level language introduces a layer of abstraction between hardware and software.
Wirth’s Law: Software is getting slower faster than hardware is getting faster.
Notes: “Wirth” is pronounced “Veert”

## Slide 72: Why This Is Important
Assembly language programming, even just a little bit of it, helps one understand how the CPU and memory operate.
People who understand how the CPU and memory operate are better able to evaluate new technologies.
People who understand how the CPU and memory operate are better able to write, or evaluate, efficient software.

## Slide 73: Questions