## Slide 1: IT 3123 Hardware and Software Concepts
Modern Computer Architecture
Notice: This session is being recorded.
Notes: Today we’re going to talk about modern computer architecture. Although modern computers are still designed in accordance with the von Neumann architecture, a lot of complexity has evolved in computer implementation since 1947.

## Slide 2: Large Memories
Modern computers have memories that can be many gibibytes.
There are usually not enough bits in an instruction word to address such large memories.
Modern computer architectures combine the instruction address field with one or more other values to make an effective address.
The effective address goes on the memory address bus.
Notes: One particular problem is that modern computers have evolved to have large memories, as much as many gibibytes.
Computer architectures still need to be backward-compatible with their predecessor architectures. That means there are usually not enough bits in an instruction word to address such large memories.
Modern computer architectures combine the instruction address field with one or more other values to make an effective address.
The effective address goes on the memory address bus. The concept of an effective address means memories much larger than implied by the number of address bits in the instruction can be used.

## Slide 3: Addressing Modes
The effective address for an instruction is the address actually used to refer to an operand.
Often forming the effective address involves computation to get enough bits to address all of memory.
Addressing modes for data access and program flow control (branching) can be different.

## Slide 4: Addressing Modes for Data
Direct address: The address in the instruction points to an operand in main memory. This could require 32 or more bits in the instruction.
Register address: The operand is held in a register. The instruction needs enough bits to address all registers, e.g., 4 bits for 16 registers, 7 bits for 128 registers.
Notes: The simplest form of addressing is direct addressing. The address from the instruction is placed on the memory address bus. That means there must be enough bits in the instruction word to address all of memory. This could require 32 or more bits in the instruction.
In register addressing the operand itself is held in a register. There is no reference to main memory. The instruction only needs enough bits to address all of the registers. If there are 16 registers, the instruction only needs four address bits. For 128 registers, seven bits are needed.

## Slide 5: Base-Displacement
Base-Displacement addressing: The effective address is formed from bits of the instruction added to the contents of a “base register.” The base register must have enough bits to address all of memory, but the number of bits in the instruction can be much smaller.

## Slide 6: Indirect Addressing
Register Indirect Addressing: The address of an operand in main memory is held in a register. The instruction needs only enough bits to select the register.
Memory Indirect Addressing: A location in main memory holds the effective address. Two memory accesses are required.
Notes: With memory indirect addressing, some method like base-displacement addressing is used to locate the “indirect” memory location. Memory indirect is largely obsolescent, but some early computers had special locations at low memory addresses that could be used in this way. Memory indirect addressing requires two memory accesses and so is expensive in execution time.

## Slide 7: Indexed Addressing
An index value, typically in a register, is added to the effective address.
Indexed addressing is used, for example, to loop through arrays.
One of the other addressing modes can be used prior to adding the index.

## Slide 8: Immediate Addressing
The operand data is held in the instruction word.
It is “immediate” because the data needed is already in the instruction register.
Example:
  addImmediate 127
Operation code “address” field

## Slide 9: Addressing for Flow of Control
Sequence is the natural operation of a von Neumann architecture computer; instructions are executed in order.
In direct addressing the full memory address of a branch target in in the instruction’s address field.
In relative addressing, address bits are added to the program counter to form the effective address. Only a few address bits are needed to address “nearby” locations.

## Slide 10: Indirect Addressing for Flow of Control
In register indirect addressing, the branch address is held in a register. Only enough address bits to enumerate the registers are needed in the instruction.
Stack indirect addressing uses the address at the top of the stack as the effective address.
Memory indirect addressing uses another form of addressing to fetch the branch address from main memory.
Notes: Stack indirect addressing may need no address bits at all in the instruction. The RETURN instruction discussed earlier is an example.

## Slide 11: Improving Performance
Faster clock speeds
Faster buses and circuits
Wider instruction and data paths
More and faster memory
Faster disks
A nanosecond is this long.

## Slide 12: Increasing Complexity
The earliest electronic digital computers were nearly as simple as TBC.
Moore’s Law allowed increasing complexity.
Hardware designers added instructions applicable to high-level languages.
By the 1970s, ALUs and control units became very complex.
Complex “machine instructions” were implemented internally as sequences of simpler operations.
Notes: TBC implements “machine” instructions as sequences of data path cycles. It is the same idea.

## Slide 13: Analysis
Analysis of actual compiled programs revealed:
  Little or no use of many complex instructions.
  Much time spent moving data to and from registers.
Conclusion: Remove complex instructions and use the transistors saved to make more registers.

## Slide 14: Reduced Instruction Set Computers (RISC)
A new approach to CPU design.
David Patterson and others.
Late 1980s to early 1990s.
Limited and simple instruction sets
Fixed length, fixed format instruction words enable pipelining, parallel fetches and executions.

## Slide 15: Reduced Instruction-Set Computers
A few kinds of instructions
A small number of instruction formats
All instructions are the same length
All operation codes are the same length
High-level language statements generally require several instructions
Emphasis is on speed

## Slide 16: RISC Instruction Formats
SPARC RISC Instruction Formats (Complete set)

## Slide 17: RISC Features
Limited addressing modes reduce complicated hardware.
Register-oriented instruction set reduces memory accesses
Large bank of registers
  Reduce memory accesses
  Efficient procedure calls

## Slide 18: Hardware and Software
Hardware and software are logically equivalent. (But there must be some hardware someplace!)
So, computer designers have a choice of implementing with hardware or software.

## Slide 19: Microprogrammed Control Unit Implementation
Microcode: programs stored in ROM that replace hardwired CPU instructions
Advantages
  More flexible
  Easier to implement complex instructions
  Can emulate other CPUs
  Can be changed!
Disadvantage
  Usually requires more clock cycles

## Slide 20: Microcode for two TBC Instructions
Notes: It is not necessary to study this in detail. The “big idea” is that the control bits necessary to decode and execute an instruction can come from read-only memory. The slide shows two examples.

## Slide 21: Hardware Implementation
Hardware implementation – operations are implemented using logic gates
Advantages:
  Speed
  RISC designs are simple and typically implemented in hardware

## Slide 22: Complex Instruction-Set Computers
Many different kinds of instructions
Many different instruction formats
Several different instruction lengths
A few different operation code lengths
Often things done in high-level languages can be performed in one instruction.
Emphasis is on flexibility

## Slide 23: CISC Instruction Formats

## Slide 24: CISC Architecture
Examples
  Intel x86, IA-32, 64; IBM Z-Series Mainframes; older CPU architectures
Characteristics
  Few general-purpose registers (perhaps 16)
  Many addressing modes
  Large number of specialized, complex instructions
  Instructions are of varying sizes

## Slide 25: Limitations of CISC Architecture
Some instructions are infrequently used by programmers and compilers
Only a few of the many instructions are used frequently
Memory references, loads and stores, are slow and account for a significant fraction of all instructions
Procedure and function calls are a major bottleneck
  Passing arguments
  Storing and retrieving values in registers
Notes: Study by Hopkins: 10 instructions accounted for 71% of code in a sample of IBM mainframe programs.

## Slide 26: CISC vs. RISC Processing

## Slide 27: CISC vs. RISC Performance Comparison
RISC  Simpler instructions
  more instructions required for a program
  more memory required to hold program, maybe
CISC  More memory access for data, so more bus traffic and increased cache memory misses
More registers would improve CISC performance but there was formerly no space available for them
Modern CISC and RISC architectures are becoming similar due to Moore’s Law.

## Slide 28: Current and Emerging Trends
CISC and RISC are re-converging because of greater chip densities.
“Multi-core” chips: 8, 16, and even more CPUs in a single integrated circuit package.
Cluster computing: Hundreds or thousands of “commodity computers” working together. Example: the “Big Mac” at Virginia Tech
Parallel computing

## Slide 29: Modern CPU Processing Methods
Separate Fetch/Execute Units.
Pipelining.
Scalar and Vector Processing.
Superscalar Processing (multiple functional units.)

## Slide 30: Separate Fetch-Execute Units
Fetch Unit
  Instruction fetch unit
  Instruction decode unit
    Determine opcode
    Identify type of instruction and operands
  Several instructions are fetched in parallel and held in a buffer until decoded and executed
  IP – Instruction Pointer register
Execute Unit
  Receives instructions from the decode unit
  Appropriate execution unit services the instruction (There can be more than one, with specialization.)

## Slide 31: Alternative CPU Organization

## Slide 32: Assembly Lines
It takes 24 to 36 hours to build a modern car.
Assembly lines produce finished cars at 50 to 100 per hour.
So, an assembly line might be “30 hours long” and might start production of a car every 60 seconds.
After 30 hours, the pipeline is full, and we get a new car every minute!

## Slide 33: Instruction Pipelining
Assembly-line technique to allow overlapping between fetch-execute cycles of sequences of instructions
Only one instruction is being completed at a time
Scalar processing
  Average instruction execution is approximately equal to the clock speed of the CPU
Problems from stalling
  Instructions have different numbers of steps
Problems of data latency
Problems from branching
Notes: Data latency: A load instruction cannot complete in one clock cycle, so the register being loaded cannot be used by the immediately following instruction.

## Slide 34: Branch Problem Solutions
Separate pipelines for both possibilities
Probabilistic approach (guess)
Requiring the following instruction to not be dependent on the branch
Instruction reordering

## Slide 35: Pipelining Example

## Slide 36: Superscalar Processing
Process more than one instruction per clock cycle…
… using multiple functional units.
Separate fetch and execute cycles as much as possible
Buffers for fetch and decode phases
Parallel execution units

## Slide 37: Superscalar CPU Block Diagram
Multiple Functional Units

## Slide 38: Scalar vs. Superscalar Processing

## Slide 39: Superscalar Issues
Out-of-order processing – dependencies (hazards)
Data dependencies
Branch (flow) dependencies and speculative execution
Parallel speculative execution or branch prediction
Branch History Table
Register access conflicts
  Logical registers (register renaming)

## Slide 40: Definitions
Multiprogramming: Two or more programs running concurrently on one computer.
Multiprocessing: A computer has two or more processors (CPUs).

## Slide 41: Multiprocessing
Motivation
  Faster computing
  More processing power
  Parallel processing
Coupling of Processors
  Tightly coupled
  Loosely coupled

## Slide 42: Tightly Coupled Systems
Shared memory and I-O
Two ways to configure:
  Master-slave multiprocessing
  Symmetric multiprocessing (SMP)

## Slide 43: Tightly-Coupled Systems
Notes: “Peripheral Component Interconnect"

## Slide 44: Symmetric Multiprocessing
Each CPU has equal access to resources
Each CPU determines what to run using a standard algorithm
Advantages
  High reliability
  Fault tolerant support is straightforward
  Balanced workload
Disadvantages
  Resource conflicts – memory, I/O, etc.
  Complex implementation

## Slide 45: Loosely-Coupled Systems
Clusters or multi-computer systems
Each system has its own CPU, memory, and I/O facilities
Advantages: Fault-tolerant, scalable, well balanced, distance is not (much of) an issue
Two ways to configure
  Shared-nothing model
  Shared-disk model

## Slide 46: Shared-Nothing Model
High speed links between nodes
No sharing of resources
Partitioning of work through division of data and message-passing
Advantage
  Reduced communication between nodes
Disadvantage
  Can result in inefficient division of work

## Slide 47: Shared Nothing Model

## Slide 48: Shared Disk Model
High speed links between nodes
Disk drives are shared between nodes
Advantage
  Better load balancing
Disadvantage
  Complex software required for transaction processing (lock, commit phases)
  Hardware complexity in the “I/O director”

## Slide 49: Shared Disk Model

## Slide 50: Advantages of Clusters
Increased computing power by combining the power of individual computer systems
Inherently scalable
Cheaper than using a single large computer
Fault-tolerance
  Failure in one node does not bring down the entire system
  Failover – processing by failed node is switched to other nodes
High Availability
Load Balancing: can be attained either through software and/or through geographically distributed location of nodes

## Slide 51: Beowulf Clusters
Simple and highly configurable
Low cost
Loosely Coupled
Computers connected to one another by a private Ethernet network
Connection to an external network is through a single gateway computer

## Slide 52: Beowulf Clusters
A type of cluster computer defined by specialized software.
Commercial-off-the-shelf components such as inexpensive computers
Blade components – computers mounted on a motherboard that are plugged into connectors on a rack
Either shared-disk or shared-nothing model

## Slide 53: Blade Computer

## Slide 54: Blade and Rack Configuration

## Slide 55: High Performance Computing
Massively parallel processor architectures (MPP)
Clusters of powerful machines or larger Beowulf blade clusters
  Well-suited for problems that can be broken into subtasks
Cloud (Grid) computing
  Supercomputer performance through distributing CPU processing to computers connected to a network

## Slide 56: Networks vs. Clusters
Externally, clusters appear as a single computing unit.
Network nodes are individually identifiable.
Workload on a cluster is determined by cluster administration and load-balancing software.
Network workload depends on the job mix of each node.

## Slide 57: Parallel Computers
Massively parallel architectures
Hundreds to millions of CPUs
CPUs have small amounts of local memory
All CPUs have access to global shared memory
Each CPU may calculate a part of the problem independently.

## Slide 58: Questions