## Slide 1: IT 3123 Hardware and Software Concepts
Review and Questions
Notice: This session is being recorded.
Notes: Time: 1:08

## Slide 2: John von Neumann
Hungarian-born American mathematician and mathematical physicist.
Many contributions to mathematics, physics, and game theory.
The short book, First Draft of a Report on the edvac, describes how most computers have been designed ever since.
That design is called the von Neumann Architecture.
Notes: Von Neumann may have been the smartest person of the 20th century and is certainly in the top ten.
Von Neumann wrote “First Draft” and only his name appears on it, but it includes the ideas of many people. It is doubtful that von Neumann meant to claim credit for those ideas, given the “first draft” title. You can read “First Draft” on line or even buy a printed copy on Amazon. https://people.csail.mit.edu/brooks/idocs/VonNeumann_EDVAC.pdf
EDVAC was “Electronic Discrete Variable Automatic Computer.”

## Slide 3: Complexity and Simplicity
Computers perform immensely complex tasks.
However, they can perform only a few, relatively simple operations (a few dozen to a few hundred).
Complexity is built out of these simple operations, which can be performed very fast.
The set of operations a particular computer can perform is called its instruction set.

## Slide 4: One Mental Model of Computing
How the CPU processes data, including:
Instructions and data
Main memory (RAM)
Computation
Input and output
Program flow (loops and if-then-else)

## Slide 5: The von Neumann Architecture
Stored program concept: Both instructions and data are stored in the same memory
Sequential execution; instructions executed in order.
Instruction cycle
  Fetch instruction
  Decode instruction
  Execute instruction
Binary numbers
The CPU, memory, and input / output are separate.

## Slide 6: Organization of the von Neumann Architecture
The central processing unit (CPU) consists of a control unit, an arithmetic-logic unit, and registers.
Memory is separate.
Input and output are separate.

## Slide 7: The Instruction Cycle
Fetch an instruction from memory.
Decode the instruction.
Execute the decoded instruction.
The instruction cycle is executed repeatedly for as long as the computer is running.

## Slide 8: The Arithmetic Logic Unit (ALU)
Performs arithmetic operations, such as addition, on data
Performs logical operations (complementation, if-statements, etc.)
Can be used to transfer data
  Within the CPU
  From CPU to I-O

## Slide 9: The Control Unit
Controls the processing of instructions by
Generating the control signals to select one operation of the ALU.
Generating control signals to send data to the ALU.
Generating control signals to store the results from the ALU.

## Slide 10: Memory
Also know as:
  RAM (Random Access Memory)
  Main memory
  Primary storage
Memory locations are of fixed size.
  Words, which are composed of several
  Bytes (octets)
Holds instructions (in machine language) and data for running programs

## Slide 11: The Little Martian Computer is a von Neumann Computer
Input and Output
Arithmetic Logic Unit
Control and Interface
Memory
Only Labels
Program Counter

## Slide 12: Problems with LMC
LMC is a decimal computer, but real computers are binary.
There is a certain amount of “magic” in the actions of the Little Martian, but no magic in real computers.
The available simulators do not show the fetch / decode / execute cycle clearly.
So… we’ll do something else!

## Slide 13: Instructions
Memory can hold both data and instructions.
Instructions consist of an operation code and one or more operands.
The operation code tells what operation the CPU is to perform.
The operands either give the location of data or contain the data.
Op code and operands are binary numbers.

## Slide 14: Instruction Set Architecture
The instruction set architecture of a computer family describes:
  The operations a computer can perform.
  The format(s) of instructions available.
  The formats of the data allowed.
Modern computer families are made backward compatible: new instructions may be added, but old programs still work.

## Slide 15: Program Flow Control
Three control structures are sufficient for all correct programs (Böhm and Jacopini, 1966)
  Sequence: one instruction after another
  Selection: if-then-else
  Iteration: loops that repeat
The program counter automatically provides sequence. (von Neumann’s design for sequential execution.)
Notes: Böhm and Jacopini’s proof is called the Structured Programming Theorem.

## Slide 16: The Branch Instruction
The branch instruction (operation code: 6) unconditionally changes the program flow.
The address part of the instruction is loaded into the program counter. (The address digits are not used to refer to data in this case.)
There are also conditional branches.
Branches implement selection and iteration.

## Slide 17: Computers Have Registers
The memory location to read or write: The memory address register
The data transferred to or from memory: The memory data register (also called the memory buffer register.)
Arithmetic results: The accumulator or data registers, also called general registers.
Address of the next instruction: The program counter
The current instruction read from memory: The instruction register

## Slide 18: A One Bit (Bit-Slice) ALU
A full adder with three inputs: a, b, ci
Three control inputs:
  Enable a
  Invert a
  Enable b
Output and co

## Slide 19: A Full ALU From Bit Slices
Overflow causes a “program check.” P and Z are stored in a latch whenever a value is stored in Acc, the Accumulator.
Notes: P, positive, is the NOT of the leftmost output bit. The leftmost bit will be one if the result is negative, so the NOT gate will produce a one or true if the result is not negative. This means zero is positive.
Z, zero, is the NOR of all four result bits. If all are zero, Z will ve true.

## Slide 20: Buses
Bus: just a bunch of conductors carrying related signals.
The buses in this diagram carry data only.
Other possibilities are, addresses, control and status.
Some buses carry power and ground.

## Slide 21: Abstraction: The ALU Symbol
C Bus
A Bus
B Bus
Control
P, Z, V

## Slide 22: The Instruction Cycle: STORE
Fetch
Decode
Execute
MAR ← PC (read memory)
Determine next operation
MDR ← A
PC ← PC+1
IR ← MDR
MAR ← IR[addr] (write memory)
Notes: Natural language description and RTL

## Slide 23: Register Transfer Example: MAR←PC
Copy
Ena A
Write
Control
P/Z Latch
Notes: On the falling edge of the clock signal, the ALU is commanded to copy, the program counter is enabled on the A bus, and a write signal is asserted on the MAR. During the clock’s low period, data travel from the PC through the ALU to the MAR. The rising edge of the clock signals the MAR to store with contents from the C bus.

## Slide 24: TBC is a Twelve-Bit Computer
Four bits of op code (So, 16 combinations.)
Eight bits of address (256 words of memory, but only 128 installed.)
Integer range from –2,048 to +2,047
It will run LMC programs (if reassembled)
Data word
Two’s Complement Integer
Instruction word
Op Code
Address
0
11
8 7

## Slide 25: “As close as we can get…”
TBC is very close to a real computer design.
  There is no magic
  There is very little hand-waving; only in how programs are loaded. (We didn’t discuss the control unit, but it’s not magic!)
In theory, you could go to the digital logic lab and build TBC.
We’ve left out power supplies, clock generator, and some details of bus design. For this course, those are “abstract details.”

## Slide 26: Elements of an Instruction
Operation Code (op-code): Commands the control unit and the ALU what to do
Operands: tell the location of the data to be used in the instruction.
  Source operand: where to get the data
  Result operand: where to put the result (Also called the destination operand.)
The operands are (usually) addresses.

## Slide 27: Operand Addresses
Addresses may be explicit or implicit
Explicit: encoded in the instruction. (The TBC memory address is explicit.)
Implicit: implied by the nature of the operand. (The TBC uses the accumulator implicitly.)
Addresses may refer to memory or to registers.
Operation code 3 25 Operand

## Slide 28: General Form of an Instruction
Op-Code
Source
Operand
Result
Operand
Op-Code
Register Operand
Memory
Operand
A More Specific Form
8 bits
4 bits
20 bits
Notes: The second form allows for only one mebibit of memory to be addressed. In a real computer, this might get added to the contents of a base register to allow addressing of large memories. Adding the operand address to the base register forms the effective address, which is the address sent to the memory address register.

## Slide 29: Instruction Format
Specific to a particular family of computers (architecture).
Specifies the length of the op-code.
And the size and number of operand fields.
A single computer may have several different instruction formats.

## Slide 30: Categories of Instructions
Data transfer instructions
Arithmetic instructions
Logical operations
Program control
Stack manipulation
I-O and machine control
Multiple-data instructions
Notes: Seven categories

## Slide 31: Memory Capacity
Limited by two factors
  Size of the MAR: k bits address 2k cells
  Size of the effective address portion of an instruction. (in LMC, it is two digits, in TLC, eight bits.)
The amount of physical memory is important for performance
Notes: “Effective address” is the address after all address arithmetic.

## Slide 32: Volatile and Non-Volatile Memories
Volatile memories lose their contents when power is removed.
Non-volatile memories retain their contents even when powered off.

## Slide 33: Error Detection: Parity
To each byte, add one extra bit, called a parity bit.
Each time the byte is stored, set the extra bit such that the number of one-bits is even. (Even parity.)
Each time a byte is read, check that the number of one bits is still even. If not, a memory error has occurred.
Could use odd parity as well.
Notes: A parity system can detect only errors in an odd number of bits. If two bits are changed erroneously, the parity will be correct even though the contents have been corrupted. Often this is called “detecting single-bit errors.”

## Slide 34: Error-Correcting Codes
Hamming code: adds extra parity bits.
Can detect double-bit errors and correct single- bit errors.
Example: d0 is checked by p0 and p1. If both are in error, then the error must be in d0.
There are other error-correcting codes.
Notes: In 1950, Richard Hamming of Bell Laboratories devised a system to detect multi-bit errors and correct single bit errors, now called
a Hamming code. The principle of the Hamming code is that every data bit is checked by more than one parity bit.
The figure shows four data bits being checked be three parity bits. If data bit d0 were corrupted, parity bits p0 and p1 would both indicate errors. The only data bit checked by both p0 and p1 is d0. If we know which single bit is incorrect, it can be corrected by complementing it, i.e. flipping it back to the other possible value. A fourth parity bit, p3, checks the parity of all the other parity and data bits. A Hamming code like this can correct single-bit errors and detect double-bit errors. The example uses four parity bits to check four data bits, an overhead of 100%. However, the overhead diminishes as the number of data bits to be checked by a Hamming code increases. A 32-bit word can be checked with seven parity bits, six of which check individual data bits and one of which checks the overall
parity.

## Slide 35: Bus Signals
3 kinds of signals and sometimes power, which is not a “signal”
  Data (binary numbers: alphanumeric, numerical, instructions)
  Addresses
  Control signals (including status)
  Power and ground (sometimes)

## Slide 36: Bus Organization in Modern CPU

## Slide 37: Memory Speed
Memory is slow compared to CPU processing speeds!
  2Ghz CPU = 1 cycle in ½ of a billionth of a second
  20ns DRAM = 1 access in 20 billionths of a second (40 times slower!)

## Slide 38: Cache Memory
A small, fast memory placed between the CPU and main memory
  Blocks: 8 or 16 bytes ; Unit of transfer between storage and cache memory. (Also called a cache line.)
Tags: point to a location in main memory

## Slide 39: Multi-level Caches

## Slide 40: Large Memories
Modern computers have memories that can be many gibibytes.
There are usually not enough bits in an instruction word to address such large memories.
Modern computer architectures combine the instruction address with one or mor other values to make an effective address.
The effective address goes on the memory address bus.

## Slide 41: Improving Performance
Faster clock speeds.
Faster buses and circuits.
Wider instruction and data paths.
More and faster memory.
Faster disks or SSDs.
A nanosecond is this long.

## Slide 42: Analysis
Analysis of actual compiled programs revealed:
  Little or no use of many complex instructions.
  Much time spent moving data to and from registers.
Conclusion: Remove complex instructions and use the transistors saved to make more registers.

## Slide 43: Reduced Instruction Set Computers (RISC)
A new approach to CPU design.
David Patterson and others.
Late 1980s to early 1990s.
Limited and simple instruction sets
Fixed length, fixed format instruction words enable pipelining, parallel fetches and executions.

## Slide 44: Reduced Instruction-Set Computers
A few kinds of instructions
A small number of instruction formats
All instructions are the same length
All operation codes are the same length
High-level language statements generally require several instructions
Emphasis is on speed

## Slide 45: Complex Instruction-Set Computers
Many different kinds of instructions
Many different instruction formats
Several different instruction lengths
A few different operation code lengths
Often things done in high-level languages can be performed in one instruction.
Emphasis is on flexibility

## Slide 46: CISC Architecture
Examples
  Intel x86, IA-32, 64; IBM Z-Series Mainframes; older CPU architectures
Characteristics
  Few general-purpose registers (perhaps 16)
  Many addressing modes
  Large number of specialized, complex instructions
  Instructions are of varying sizes

## Slide 47: CISC vs. RISC Performance Comparison
RISC  Simpler instructions
  more instructions required for a program
  more memory required to hold program, maybe
CISC  More memory access for data, so more bus traffic and increased cache memory misses
More registers would improve CISC performance but there was formerly no space available for them
Modern CISC and RISC architectures are becoming similar due to Moore’s Law.

## Slide 48: Current and Emerging Trends
CISC and RISC are re-converging because of greater chip densities.
“Multi-core” chips: 8, 16, and even more CPUs in a single integrated circuit package.
Cluster computing: Hundreds or thousands of “commodity computers” working together. Example: the “Big Mac” at Virginia Tech
Parallel computing
Experimental architectures

## Slide 49: Modern CPU Processing Methods
Separate Fetch/Execute Units
Pipelining
Scalar and Vector Processing
Superscalar Processing

## Slide 50: Instruction Pipelining
Assembly-line technique to allow overlapping between fetch-execute cycles of sequences of instructions
Only one instruction is being completed at a time
Scalar processing
  Average instruction execution is approximately equal to the clock speed of the CPU
Problems from stalling
  Instructions have different numbers of steps
Problems of data latency
Problems from branching
Notes: Data latency: A load instruction cannot complete in one clock cycle, so the register being loaded cannot be used by the immediately following instruction.

## Slide 51: Superscalar Processing
Process more than one instruction per clock cycle…
…using multiple functional units.
Separate fetch and execute cycles as much as possible
Buffers for fetch and decode phases
Parallel execution units

## Slide 52: Superscalar CPU Block Diagram
Multiple Functional Units

## Slide 53: Definitions
Multiprogramming: Two or more programs running concurrently on one computer.
Multiprocessing: A computer has two or more processors (CPUs).

## Slide 54: Peripheral Devices
I-O devices are sometimes called “peripheral devices.”
They can be thought of as forming the periphery (edge area)of a computer system.

## Slide 55: I-O Issues
Several devices can perform I/O simultaneously.
Unexpected (asynchronous) input.
Various input formats.
Status information needed for each device.
Actual I-O is almost always performed by the operating system on behalf of applications.
Notes: More than one device can input or output at the same time. I can have input arrive unexpectedly. The mouse is just sort of sitting there - and I can reach down and move it and generate input.
I get various input formats. We talked about that some when we talked about data formats in about the third class of the semester. For every i/o device I need some information about the status of the device.
If the printer is jammed and the buffer is full, and I send one more byte that will be lost - the CPU and the operating system need to know that so that they don’t send that one more byte that will be lost.

## Slide 56: Memory Mapped I-O
Some computer architectures reserve memory locations for input and output.
No special I-O instructions needed.
“Writing to memory” sends data to an output device.
“Reading” from memory gets data from an input device.
Memory locations are also reserved for status and command information
Notes: In memory-mapped I/O, some of the addresses that would otherwise be part of main memory instead refer to device registers. Often these addresses are at the highest part of the logical address space, where one might not expect actual memory to be installed in any case. It is up to the address decoder to sort out which addresses are actual memory locations and which refer to device registers.

## Slide 57: Port Mapped I-O
Modern computers are more likely to have a separate address space for I-O devices.
That allows the full memory address space to be used for memory,
…but requires separate I-O instructions.
Some early designs used both, with display memory addressed as part of the main memory address space. Unusual now.
Notes: In port-mapped I/O, there is a separate address space of I/O ports. This has the advantage of allowing the full physical memory address space to be used for memory and of separating I/O devices, which are usually slower than memory, from the operation of the memory subsystem. The disadvantage is that separate instructions for input and output are needed, as with the Intel X86 IN and OUT instructions

## Slide 58: I-O Speed Considerations
CPU operates at speeds much faster than the fastest I-O device:
  CPU: nanoseconds
  I-O: milliseconds
  Difference: 106, CPU is about a million times faster than devices like magnetic disks.
Devices operate at different speeds.
Some devices produce bursts of data.
Block data transfer required for disks and certain other devices.
Notes: The CPU operates faster than memory and very much faster than even the fastest I/O device.
I/O devices operate at different speeds and they may either generate or consume bursts of data. And in some cases like disk devices when I read a block off the disk I know how many blocks I am going to transfer - maybe 512 bytes - but I have to do them all in one block. Otherwise the disk will have spun out from under the read head and the remaining bytes in that block won’t be available until the next time the disk spins around.
You think about a disk spinning at 7200 or 15000 rpm and you might decide the next time is going to come pretty soon but remember that you are comparing the time for that one disk rotation with millions of CPU cycles so we dare not miss that block transfer.

## Slide 59: Interrupts
Interrupt: an electronic signal that causes the CPU to alter its normal flow of instruction execution.
Frees CPU from waiting for events.
Provides control for external input.
Notes: In order to go further - we need this idea of an interrupt.
An interrupt is an electronic signal that causes the CPU to alter it’s instruction flow. If I have this idea of an interrupt I can get rid of the idea of the CPU waiting for the keyboard controller to read a key - I can instead command the controller to read a key raise an interrupt signal. The CPU then can do other work while waiting for input from the controller.

## Slide 60: Approaches to I-O Transfers
Programmed I-O with busy waiting:
  Uses the CPU to control I-O
  CPU cannot do anything else while I-O is in process.
Interrupt-driven I-O:
  CPU commands an I-O device to do something.
  Device raises an interrupt signal when done
  CPU can do other work.
Direct Memory Access (DMA) I-O.
Notes: We’ve talked about two approaches to I/O processing already - programmed I/O is busy waiting the CPU is doing all of the work and can’t do anything else while I/O is in process.
The second one that we’ve talked about is interrupt driven I/O. The CPU sets up the I/O but then the device raises an interrupt when it is done and the CPU can do other work between the time it starts the I/O operation and the time the interrupt arrives to say it is done.
The third one is almost always used for disk-like devices and maybe other direct memory access (or DMA I/O) devices.

## Slide 61: Avoiding Conflicts
What happens if two programs want to do I-O at the same time. (Big trouble!)
Solution: privileged instructions allow only the operating system to do I-O:
  A program requests an I-O operation from the operating system.
  The operating system “blocks” the program.
  The operating system does the I-O.
  The operating system unblocks the program.
Notes: The other condition of conflict might be two or more programs that want to do I/O at the same time.
I want you to think about a specific case of that. I have my disk head here with a disk spinning around underneath and I have positioned it carefully over the track I am about to write.
And the disk spins around and I send a write signal and just about that time some other program moves the disk head. What has happened?
Corrupted disk - my data are gone forever.
They are written to the disk - but I have no clue where they are so they might just as well be gone forever. And something that used to be on the disk is not there anymore.
The Pick operating system, which is thankfully obsolete, had that problem. The condition was called a group format error abbreviated GFE and anyone who had to work with Pick knew that meant gone forever.
The solution in modern operating system is that we don’t let programs do I/O. Only the operating system does I/O. That way the operating system can serialize those I/O operations and keep situations like the one I described from happening.
A program is going to request an I/O operation and it does that with one of those software interrupts - a system call interrupt.
So I set up a system call instruction that says I want to do I/O from this device and this memory location and it is either read or write.
Executing that instruction generates an interrupt. The operating system gets control. The operating system then blocks the program in the sense that my expectation is that the I/O will be finished when the instruction after the system call is executed. And we would like that expectation to be true by not allowing anymore instructions from that particular program to execute until the I/O is finished. So the operating system blocks the program, performs the I/O and once everything is done and the dust has settled, the operating system unblocks the program that requested
I/O and everyone is happy.

## Slide 62: Primary and Secondary Storage
Primary storage: registers, cache memory, main memory. Usually volatile.
Primary storage holds instructions and data for currently running programs.
Secondary storage: disks, optical drives, tape. Non-volatile.
Secondary storage generally holds “files” which may be data or executable machine code.

## Slide 63: Storage Speed
Measured by access time and data transfer rate.
Access time: average time it takes a computer to locate data.
  nanosecond = one-billionth of a second
  millisecond = one-thousandth of a second
Data transfer rate: amount of data that moves per second.

## Slide 64: Hierarchy of Storage
Access time
1-20 nanoseconds
½ nanosecond
20-60 nanoseconds
0.1 millisecond
10 milliseconds
100 milliseconds
Seconds to minutes
Minutes to hours
Difference of 1,000,000 (106)

## Slide 65: Magnetic Disk Technology
One or more platters.
Each platter has two heads, two recording surfaces.
Each surface has ≈1,000 concentric tracks.
Each track is divided into fixed size blocks of 512 or 4,096 bytes. Also erroneously called sectors.

## Slide 66: Disk Access Time
Seek time: time required to move heads to the desired track.
Rotational latency: time required for disk to rotate to beginning of correct block.
Transfer time: time required to transfer a block of data to the disk controller buffer.

## Slide 67: Multiple Zone Recording
Modern disks solve the recording density problem by having more blocks per track at the outer edge than near the center. A typical disk might have a dozen or so such “zones.”

## Slide 68: Solid State Drives
Can directly replace magnetic disks mechanically and electrically.
No moving parts.
Flash memory.
Data is organized in pages within blocks.
Reading is at the page level, writing at block level.
Wear-leveling used to extend life.
Controller logic used to manage memory space and provide fast reads/writes.

## Slide 69: Redundant Data Storage
If redundant (duplicative) data are stored on two or more disks, the failure of any single disk will not cause data loss.
RAID = redundant array of inexpensive disks.
“Levels” of RAID
  RAID 1: Mirrored disk volumes
  RAID 5: Bits of each data word duplicated across three or more drives.
  There are other levels.

## Slide 70: RAID is not ‘Backup’
RAID protects against disk hardware failure by storing redundant bits on more than one disk.
It does not protect against other causes of data loss:
  File accidentally deleted.
  Program error corrupts / destroys data.
  Fire or other disaster.
  Etc.

## Slide 71: The End of RAID
When a drive in a RAID 5 array fails, the array keeps working…
… but it’s not redundant anymore!
The failed drive must be replaced, and the array re-built before any other drive failure.
Large drives make the rebuild time longer.
The longer the rebuild time, the greater the chance of a catastrophic failure.

## Slide 72: Magnetic Tape
Offline and “near-line” storage
Archival purposes
Disaster recovery
Tape Cartridges
  20 – 144 tracks (side by side)
  Read serially
  “Smart” tapes
Tape “libraries” and auto-loaders

## Slide 73: LCD Displays
Fluorescent backlight panel.
3 color cells per pixel.
Operation
  1st filter polarizes light in a specific direction
  Electric charge rotates molecules in liquid crystal cells proportional to the strength of each color signal, changing polarization.
  Color filters only let through red, green, and blue light.
  Final filter lets through light with brightness proportional to the polarization twist.

## Slide 74: Organic LED (OLED) Displays
Made with organic compounds that emit red, green, or blue light.
No backlight needed.
No mechanical change as with liquid crystals, so response time of a millisecond or less.

## Slide 75: Touchscreens
Capacitive touch screens are most common, depend on the fact that the human body is a conductor of electricity.
Contact is reported as X-Y coordinates.
Single-touch and multi-touch screens are available.
Motion sensing is available.
Notes: The alternative to a capacitive touchscreen is a resistive touchscreen, described in the textbook.

## Slide 76: Printers
Dots vs. pixels
  300-2400 dpi vs. 70-100 pixels per inch
  Dots are on or off, pixels have intensities
Types
  Inkjet – squirts heated droplets of ink
  Laser – xerographic imaging
  Thermal wax transfer
  Dye Sublimation
  Older technologies
    Dot matrix, fully-formed characters
}
Color technologies

## Slide 77: Keyboards
Usually connected wirelessly or via USB.
Pressing a key generates a scan code.
Releasing a key generates a different scan code.
Different codes for press/release make key “chords” and repeating keys possible.
Scan codes are translated to characters by the operating system.
Notes: Wireless connections can be Bluetooth or operate in the WiFi bands. They could also use an infrared connection, similar to some remote controls.
Keystrokes are converted to electrical signals in several ways:
Membrane keyboard
Dome-switch keyboard
Scissor-switch keyboard
Capacitive keyboard
Mechanical-switch keyboard
Hot-swappable keyboard
Buckling-spring keyboard
Hall-effect keyboard
Internal circuitry must “debounce” the signal no matter what kind of switch is used. Keyboard circuitry also provides for “rollover,” the case where the next key in a sequence if presses before the current one is completely released. Keyboards may provide tacticle and audible feed backt to the typist.

## Slide 78: Mice and Pointers
Mice and other pointing devices translate motion in two dimensions into position of a cursor on a screen.
Translation from “increments” to cursor position is done by the operating system.
Mice may also have buttons and scroll wheels.
Connectivity is usually wireless or USB.
Doug Englebart’s mouse. Courtesy SRI International.

## Slide 79: Questions