## Slide 1: IT 3123 Hardware and Software Concepts
Combinational Circuits
Notice: This session is being recorded.
Notes: Time 1:13 including announcements.
Spring 2024: 50 minutes

## Slide 2: Logic Diagrams
Logic diagrams are abstractions of logic circuits.
Gate symbols represent corresponding gates.
Lines represent connections: wires, traces on a printed circuit board, or conductors within a chip.
Power and ground connections are omitted.
Connections are shown with a heavy dot.
No dot means no connection.

## Slide 3: Combinational Circuits
A combinational circuit is a digital logic circuit the output of which is determined solely by its inputs.
Implication: combinational circuits have no memory.

## Slide 4: Computation with Digital Logic
Boolean algebra deals with operations on binary digits and produces binary digit results.
Arithmetic operations like addition can be expressed as truth tables.
You can build a digital logic circuit to compute any function for which you can write the truth table. We will see how shortly.

## Slide 5: “A computer that cannot add is unthinkable.”
The IBM Model 1620, a scientific computer of the 1960s, could not add.
Instead, it used a table lookup to find sums.
It was said that IBM’s code name for the 1620, CADET, meant “Can’t Add, Doesn’t Even Try.”
Notes: It was Andrew Tanenbaum who wrote “a computer that cannot add is unthinkable.”

## Slide 6: Reminder: Binary Addition
0 0 1 1 0 1 0 1 0 1 1 10




At the moment, we are interested only in the sum, and not in the carry.
a b s

## Slide 7: Binary Addition: Sum
This is the EXCLUSIVE OR function
a  b
a
b
Rewrite the sum as a truth table.
a | b | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 8: Binary Addition: Carry
This is the and function
a
b
ab
Rewrite the carry as a truth table.
a​ | b​ | c0
0​ | 0​ | 0​
0​ | 1​ | 0​
1​ | 0​ | 0​
1​ | 1​ | 1​
Notes: It is called co because it is the carry out.

## Slide 9: A Half-Adder
a b
sum
carry

## Slide 10: Circuit Analysis
a b
sum
carry
How do we know this computes sum and carry?
a​ | b​ | c0
0​ | 0​ | 0​
0​ | 1​ | 0​
1​ | 0​ | 0​
1​ | 1​ | 1​
a | b | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 11: Binary Addition with Carry In
1 0 0 1 1 1 0 1 0 1 1 0 1 1 10 11




The first three of these are obvious. The fourth one is just 1+1=2
The last one is needed when you have a carry in. It is 1+1+1=3



## Slide 12: Addition with Carry In as Truth Table
a | b | ci | s | co
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Inputs Outputs
Notes: We now have eight rows because there are three input variables, and 23 is 8.

## Slide 13: Computation of the Sum
The sum is 1 when the number of input ones is odd. s=(a  b)  ci
a | b | ci | s | co
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 14: Circuit for the Sum
s=(a  b)  ci
a b
ci
Sum
V
W
V computes a  b W computes V  ci

## Slide 15: Computation of the Carry Out
Carry out is true when both a and b are true or when ci and one of a and b is true: co=a•b+(a  b) •ci
a | b | ci | s | co
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 16: Add the Carry Out
V computes a  b X computes a•b Y computes (a  b)• ci
co=a•b+(a  b) •ci
a b
ci
V
W
X
Y
Sum
co
co
Notes: The trouble with this is that there are two carry-outs, and gates X and Y.

## Slide 17: The Full Adder
Z computes X + Y
a b
ci
V
W
X
Y
Z
Sum
Carry out
Notes: An OR gate, Z, combines the two carry-outs. If either or both is true, carry out from the addition is true or one.

## Slide 18: Full Adder: Two Half Adders
Two Half-Adders and an OR gate
Notes: Another way of thinking about the full adder is that it’s two half-adders. One computes the sum of the inputs, and the other adds carry-in to the sum. The OR gate combines the two carry out possibilities.

## Slide 19: Abstraction
Full Adder
A
B
Ci
Co
S

## Slide 20: Four Bit Ripple-Carry Adder
Full Adder
Full Adder
Full Adder
Full Adder
0
Carry Out
a0 b0
a1 b1
a2 b2
a3 b3
s0
s1
s2
s3

## Slide 21: About Digital Logic Gates
The output of a digital logic gate depends only upon its inputs; changing the inputs changes the output.
The transistors in a digital logic gate take a few nanoseconds (billionths of a second) to switch from on to off or vice-versa.
The gate delay of a digital logic gate is the time for a change in inputs to be reflected in a new output.
Notes: There is also a propagation delay, the time for the output of one gate to reach the input of the next one. Propagation occurs at 50 to 99% of the speed of light.

## Slide 22: Gate Delay in Ripple-Carry Adder
Full Adder
Full Adder
Full Adder
Full Adder
0
Carry Out
a0 b0
a1 b1
a2 b2
a3 b3
s0
s1
s2
s3
5 ns
5 ns
5 ns
5 ns
Notes: All four adders are computing continuously, but do not produce a correct output until the inputs and carries have propagated all the way through the circuit. If each full adder takes 5 ns for gate delay and propagation time, then the carry in to full adder 1 isn’t accurate until about 5 ns after the inputs to full adder 0 are stable.

## Slide 23: No Such Thing as a Free Lunch
Four Bit Carry Anticipation Adder
Trex4321
Notes: https://commons.wikimedia.org/wiki/File:Four_bit_adder_with_carry_lookahead.svg
https://github.com/hneemann/Digital

## Slide 24: Gates with Multiple Inputs
This
Represents this

## Slide 25: Sum-of-Products Method
Generates a correct circuit for any truth table.
Provide a not gate for each variable.
Provide an and gate for each row in the truth table where the result is 1. (These are the product terms.) The and gates must have an input for each variable.
Connect the and gates according to the product terms.
Connect all and gate outputs to an or gate.
Notes: Gates with more than two inputs are possible. An abstraction for thinking about them is as a

## Slide 26: Example: The Majority Function
The majority function is one (true) when there are more ones than zeroes in a row.
We are interested in the rows where the result, F, is one.
That is F = A•B•C + A•B•C + A•B•C + A•B•C
This is the minterm form; simpler expressions may be possible.
A | B | C |  | F
0 | 0 | 0 |  | 0
0 | 0 | 1 |  | 0
0 | 1 | 0 |  | 0
0 | 1 | 1 |  | 1
1 | 0 | 0 |  | 0
1 | 0 | 1 |  | 1
1 | 1 | 0 |  | 1
1 | 1 | 1 |  | 1

## Slide 27: Provide not Gates

## Slide 28: Provide and Wire and Gates
The first product term is A•B•C

## Slide 29: Wire the Remaining and Gates
A•B•C
A•B•C
A•B•C
A•B•C

## Slide 30: Provide an or gate for the Output
A | B | C |  | F
0 | 0 | 0 |  | 0
0 | 0 | 1 |  | 0
0 | 1 | 0 |  | 0
0 | 1 | 1 |  | 1
1 | 0 | 0 |  | 0
1 | 0 | 1 |  | 1
1 | 1 | 0 |  | 1
1 | 1 | 1 |  | 1
F = A•B•C + A•B•C + A•B•C + A•B•C
F

## Slide 31: Digital Logic Building Blocks
As complex as digital logic is, there are a few fundamental building blocks.
These building blocks get combined in various ways to build more complex structures.
Modern computer designs depend in large part on relatively few digital logic building blocks like these in the same way that modern buildings depend on a few standard sizes for things like lumber, bricks, and doors.

## Slide 32: Decoders
In Chapter 3 we will find that instructions at the machine level include an operation code, or op code, that tells what the computer should do.
This op code gets decoded into several signals that control the CPU.
A decoder takes an n-bit binary number and produces one of n signals.

## Slide 33: Building a Decoder
One-bit decoder
1
Two to Four Decoder
1
0
1
0
1
0

## Slide 34: Multiplexers
An n-bit control signal selects one of 2n inputs.
The selected input is connected to the output.
C1
C0
I0
I1
I2
I3
Output
0 1

## Slide 35: Building a Multiplexer
I3
I2
I1
I0
C0
C1
S0
S0
S1
S1
Output

## Slide 36: Shifting
You can multiply a decimal number by 10 by adding a zero on the right, effectively shifting all the digits left one place.
You can divide by 10 by chopping off a digit on the right, shifting right. The digit chopped off is the remainder.
Binary numbers can be multiplied or divided by two in the same way.

## Slide 37: Multiply or Divide by Two
These are “wired shifts.”
Left Shift Multiply by 2
Right Shift Divide by 2

## Slide 38: A Controlled Shifter

## Slide 39: Arithmetic and Logical Shifts
Notes: Arithmetic shift right preserves the sign bit, logical shift right supplies a zero on the left.

## Slide 40: Other Building Blocks
There are a few other building blocks.
We’ll see some of them in the next class.
It is possible, perhaps even likely, that the existence of these standard building blocks explains why hardware designs have far few errors than software designs.

## Slide 41: A Word About Chips
Small-scale integration packages gates.
Medium-scale integration packages simple functions.
Large-scale and Very large-scale integration package complex functions or complete systems.
Notes: In this case, “package” is a verb.

## Slide 42: Questions