## Slide 1: IT 3123 Hardware and Software Concepts
Computer and Memory Organization
Notice: This session is being recorded.

## Slide 2: Instructions
Direction given to a computer
Cause electrical signals to be sent through specific circuits for processing
Instruction Set: The collection of instructions a given computer can perform. (TBC has nine instructions; the list of them is its instruction set.)

## Slide 3: Instruction Set
Design defines functions performed by the processor
Differentiates computer architecture by the
  Number of instructions
  Complexity of operations performed by individual instructions
  Data types supported
  Format (layout, fixed vs. variable length)
  Use of registers
  Addressing (size, modes)

## Slide 4: Elements of an Instruction
Operation Code (op-code): Commands the control unit and the ALU what to do
Operands: tell the location of the data to be used in the instruction.
  Source operand: where to get the data
  Result operand: where to put the result (Also called the destination operand.)
The operands are (usually) addresses.

## Slide 5: Operand Addresses
Addresses may be explicit or implicit
Explicit: encoded in the instruction. (The TBC memory address is explicit.)
Implicit: implied by the nature of the operand. (The TBC uses the accumulator implicitly.)
Addresses may refer to memory or to registers.
Operation code 3 25 Operand

## Slide 6: General Form of an Instruction
Op-Code
Source
Operand
Result
Operand
Op-Code
Register Operand
Memory
Operand
A More Specific Form
8 bits
4 bits
20 bits
Notes: The second form allows for only one mebibit of memory to be addressed. In a real computer, this might get added to the contents of a base register to allow addressing of large memories. Adding the operand address to the base register forms the effective address, which is the address sent to the memory address register.

## Slide 7: Instruction Format
Specific to a particular family of computers (architecture).
Specifies the length of the op-code.
And the size and number of operand fields.
A single computer may have several different instruction formats.

## Slide 8: Categories of Instructions
Data transfer instructions
Arithmetic instructions
Logical operations
Program control
Stack manipulation
I-O and machine control
Multiple-data instructions
Notes: Seven categories

## Slide 9: Data Transfer Instructions
Move data between registers in CPU
Transfer data from memory to a CPU register (load)
Transfer data from a CPU register to memory (store)
Size of a single transfer: generally, the size of a data register; a “word”
Words are 8, 16, 32, 64, or 128 bits
64-bit words are currently most common

## Slide 10: Arithmetic Instructions
The usual suspects: + – / *
Separate instructions for integer and floating-point operands.
Shift and rotate instructions
  One bit shift left multiplies by two
  One bit shift right divides by two
Rotate: Bits shifted out one end are used for replacement bits at the other end.
Increment, complement, etc.

## Slide 11: Logical Operations
Logical AND and OR of two operands
Sometimes others: XOR, NOR, NOT
Relational operations: > < =
Testing for zero, positive, negative

## Slide 12: Program Control
Branch instructions; conditional and unconditional, do not save the program counter. Program logic must set return.
Call instructions save the program counter someplace.
Main Program
1024 1025 1026 CALL A 1027
1027
Save area:

## Slide 13: Subroutine Linkage Problem
Method A calls Method B.
Main Program
1024 1025 1026 CALL A 1027
Method A
2048 2049 CALL B 2050 2051 RETURN
2050
Save area:
Oops! Main program’s return address is lost!
Notes: Calling methods (subroutines or subprograms) we have the same problem as Hansel und Gretel; getting there is no problem, but how to get back?

## Slide 14: Subroutine Linkage Solution
Dynamic allocation of data…
… so that multiple return addresses can be saved.
Data structure: last-in, first-out, so that retrieving an address gets that of the most recent subprogram call.
In computer terms, that’s a stack.

## Slide 15: Stack During Subprogram Call
Main Program
1024 1025 1026 CALL A 1027
1027
The CALL instruction pushes the program counter on the stack before branching to the address of method A. Remember: the program counter holds the address of the next instruction.
PUSH PC
PC  address(A)
Notes: Let’s see an example of that. Machines with stacks have PUSH and POP instructions. PUSH places the current value on top of the stack and, if necessary, moves everything else down, like placing a tray on that stack of trays in the cafeteria. POP removes the item at the top of the stack and moves the others up. When you take the top tray from that stack, you get the one most recently placed on top. The one below that becomes the new top. PUSH and POP can be used to save and restore data, but they’re most useful in subprogram linkage.
When the main program encounters CALL A, the program counter, which holds the address of the next instruction, is pushed onto the stack, then the address of method A is loaded into the program counter.
After the call instruction, the top of the stack is the address of the NEXT instruction in the main program.

## Slide 16: After Subprogram Call
Main Program
1024 1025 1026 CALL A 1027
1027
Method A
2048 2049 CALL B 2050 2051 RETURN
Method A executes.
Notes: Because the address of method A was loaded into the program counter register after saving the return address on the stack, method A runs. It contains a call to Method B.

## Slide 17: A Second Subprogram Call
Main Program
1024 1025 1026 CALL A 1027
Method A
2048 2049 CALL B 2050 2051 RETURN
The CALL instruction saves (pushes) the program counter on the stack before branching to the address of method B.
PUSH PC
PC  address(B)
1027
1027
2050
Notes: When method A calls method B, the program counter, which contains the address of the next instruction, in this case, 2050, is pushed onto the stack. * The address 2050 is now at the top of the stack. After the program counter has been saved on the stack, the address of method B is put into the program counter register, so the next instruction will be the first instruction of method B.

## Slide 18: Execution of Method B
Main Program
1024 1025 1026 CALL A 1027
Method A
2048 2049 CALL B 2050 2051 RETURN
1027
2050
Method B
4096 4097 4098 4099 RETURN
Method B executes.
Notes: Method B runs. It doesn’t contain any calls, although it could. It does contain a RETURN instruction. Let’s look at how that works.

## Slide 19: Method B Returns to Method A
Main Program
1024 1025 1026 CALL A 1027
Method A
2048 2049 CALL B 2050 2051 RETURN
Method B
4096 4097 4098 4099 RETURN
1027
2050
The RETURN instruction pops the return address from the stack and stores it in the program counter. Control returns to method A.
PC  POP
Notes: The return instruction in method B pops * the return address from the top of the stack and puts it in the program counter register. * It is the address in method A immediately after the CALL B instruction, so method A continues at the point right after the call instruction.

## Slide 20: Method A Returns to Main Program
Main Program
1024 1025 1026 CALL A 1027
Method A
2048 2049 CALL B 2050 2051 RETURN
Method B
4096 4097 4098 4099 RETURN
1027
The RETURN instruction pops the return address from the stack and stores it in the program counter. Control returns to The main program.
PC  POP
Notes: The RETURN instruction in method A works the same way. The address at the top of the stack is 1027. * It is popped off the stack and stored in the program counter register. * At the beginning of the next instruction cycle, the instruction immediately after CALL A in the main program will be executed.

## Slide 21: I-O and Machine Control
Transfers from registers to I-O devices
Direct memory access (DMA) I-O The I-O device communicates with memory independent of the CPU
Machine state switching (privileged instructions)
Interrupt control
State saving
Halt

## Slide 22: Multiple-Data Instructions
Perform the same operation on multiple data items simultaneously (Example: Intel MMX)
Commonly used in vector and array processing
SIMD: Single-instruction, multiple data

## Slide 23: Multiple Data Instructions

## Slide 24: Memory Capacity
Limited by two factors
  Size of the MAR: k bits address 2k cells
  Size of the effective address portion of an instruction. (in LMC, it is two digits, in TLC, eight bits.)
The amount of physical memory is important for performance
Notes: “Effective address” is the address after all address arithmetic.

## Slide 25: Operation of Memory
Notes: Remember, a decoder has an input of n bits and selects one of 2n outputs.

## Slide 26: Decoders for Large Memories
A 32-bit MAR would need a 32 to four billion decoder; not really practical.
If the address is divided into 16 bits of “row address” and 16 bits of “column address,” each is 216 = 65,536 lines.
Decoding is necessarily slower for very large memories.
Decoding happens within the memory chips, not in the CPU. That keeps the size of the memory address bus reasonable.

## Slide 27: Volatile and Non-Volatile Memories
Volatile memories lose their contents when power is removed.
Non-volatile memories retain their contents even when powered off.

## Slide 28: Random Access Memory (RAM)
Called “random access” because any cell may be addressed as fast as any other.
Dynamic RAM (DRAM)
  Loses contents when power removed (volatile).
  Must be refreshed thousands of times per second..
Static RAM (SRAM)
  More expensive, faster, no refresh needed.
  Loses contents when power removed(volatile).
SDRAM: Synchronous dynamic RAM.
Notes: SDRAM uses a clock to synchronize the operation of the memory.

## Slide 29: Flash Memory
Non-volatile semiconductor memory
Faster than magnetic disks but more expensive
Uses
  BIOS: initial boot instructions and diagnostics
  Solid-state drives
  Digital cameras, music players, thumb drives, etc.
Slower than RAM
Limited, but fairly large, number of write cycles.

## Slide 30: Read Only Memory (ROM)
Non-volatile memory to hold software that is not expected to change over the life of the system
ROM: Contents fixed when manufactured; cannot be changed.
EEPROM
  Electrically Erasable Programmable ROM
  Slower and less flexible than flash memory
  Used when changes are infrequent

## Slide 31: CMOS Memory
CMOS: Very low power read-write memory; clock and configuration info.
CMOS: Complementary metal-oxide semiconductor.

## Slide 32: Boundary Alignment
Modern computers are byte-addressable, i.e. a program can request any byte.
Transfers between CPU and memory are in words. For a 64-bit CPU, that’s eight bytes.
Data items more than one byte and less than one word should be word-aligned so that only one transfer is needed.
Compilers do this automatically.

## Slide 33: Byte Ordering
The most significant byte of a word can be stored:
  At the lowest address or
  At the highest address.
This is a choice made when the architecture is designed.
  Lowest address called : Big-endian
  Highest address called: Little-endian
Important for data exchange.
Notes: The terms big endian and little endian come from Jonathan Swift’s Gulliver’s Travels, and refer to the
war over which end of an egg to open. They were applied to computer byte ordering by D. Cohen (1981).

## Slide 34: Error Detection: Parity
To each byte, add one extra bit, called a parity bit.
Each time the byte is stored, set the extra bit such that the number of one-bits is even. (Even parity.)
Each time a byte is read, check that the number of one bits is still even. If not, a memory error has occurred.
Could use odd parity as well.
Notes: A parity system can detect only errors in an odd number of bits. If two bits are changed erroneously, the parity will be correct even though the contents have been corrupted. Often this is called “detecting single-bit errors.”

## Slide 35: Error-Correcting Codes
Hamming code: adds extra parity bits.
Can detect double-bit errors and correct single- bit errors.
Example: d0 is checked by p0 and p1. If both are in error, then the error must be in d0.
There are other error-correcting codes.
Notes: In 1950, Richard Hamming of Bell Laboratories devised a system to detect multi-bit errors and correct single bit errors, now called
a Hamming code. The principle of the Hamming code is that every data bit is checked by more than one parity bit.
The figure shows four data bits being checked be three parity bits. If data bit d0 were corrupted, parity bits p0 and p1 would both indicate errors. The only data bit checked by both p0 and p1 is d0. If we know which single bit is incorrect, it can be corrected by complementing it, i.e. flipping it back to the other possible value. A fourth parity bit, p3, checks the parity of all the other parity and data bits. A Hamming code like this can correct single-bit errors and detect double-bit errors. The example uses four parity bits to check four data bits, an overhead of 100%. However, the overhead diminishes as the number of data bits to be checked by a Hamming code increases. A 32-bit word can be checked with seven parity bits, six of which check individual data bits and one of which checks the overall
parity.

## Slide 36: Buses
The physical connection that makes it possible to transfer data from one location in the computer system to another
Group of electrical conductors for carrying signals from one location to another
Line: each conductor in the bus

## Slide 37: Bus Signals
3 kinds of signals and sometimes power, which is not a “signal”
  Data (binary numbers: alphanumeric, numerical, instructions)
  Addresses
  Control signals (including status)
  Power and ground (sometimes)

## Slide 38: Bus Applications
Connect CPU and Memory
I/O peripherals: on same bus as CPU/memory or separate bus
Physical packaging commonly called backplane or motherboard
  Also called system bus or external bus
  Example of broadcast bus
  Part of printed circuit board called motherboard that holds CPU and related components

## Slide 39: Bus Hierarchy
Processor bus: on-chip
Memory bus (northbridge) Connects the memory subsystem and processor
I/O bus (southbridge)
  Connects I/O to the CPU and memory
  Connects all peripheral cards and connectors
  Examples: SATA, Thunderbolt, and USB

## Slide 40: Motherboard

## Slide 41: Bus Characteristics
Protocol
  Documented agreement for communication
  Specification that spells out the meaning of each line and each signal on each line
Throughput, i.e., data transfer rate in bits per second
Data width in bits carried simultaneously

## Slide 42: Parallel Buses
High throughput because all bits of a word are transmitted simultaneously.
Expensive and require physical space
Subject to electrical interference, which limits their speed and length.
“Bus skew” is the condition that bits on some of the lines arrive before bits on other lines.
If bus skew exceeds one bit time, data are corrupted!
Generally used for short distances such as CPU buses and on computer motherboards.

## Slide 43: Serial Buses
One bit transmitted at a time; so, no skew.
Single data line pair and a few control lines.
For many applications, throughput is higher than for parallel because of lower electrical interference and absence of skew.
Consider USB (Universal Serial Bus) and SATA (Serial ATA disk attachment).

## Slide 44: PCI Express (PCIe)
A serial/parallel computer expansion (internal) bus
Full duplex operation over two simplex paths, one each direction.
Each pair is a “lane.”
A “link” may be one to 32 lanes.
Lanes transmit byte streams
https://en.wikipedia.org/wiki/PCI_Express

## Slide 45: Point to Point vs. Multipoint
cv
CPU
PCIe Root Complex
Point-to-point
Computer
Computer
Printer
Multipoint

## Slide 46: Bus Organization in Modern CPU

## Slide 47: Virtual Memory
What if a program (or collection of programs) needs more memory than the computer has?
Solution: use disk as a substitute for memory
Managed by the operating system
Built into the hardware
Independent of application (transparent)

## Slide 48: Memory Speed
Memory is slow compared to CPU processing speeds!
  2Ghz CPU = 1 cycle in ½ of a billionth of a second
  20ns DRAM = 1 access in 20 billionths of a second (40 times slower!)

## Slide 49: Memory Enhancements
Methods to improve memory accesses
  Wide Path Memory Access
    Retrieve multiple bytes instead of one byte at a time
  Memory Interleaving
    Partition memory into subsections, each with its own address register and data register
  Cache Memory

## Slide 50: Memory Interleaving

## Slide 51: Cache Memory
A small, fast memory placed between the CPU and main memory
  Blocks: 8 or 16 bytes ; Unit of transfer between storage and cache memory. (Also called a cache line.)
Tags: point to a location in main memory

## Slide 52: Cache Memory
Hit Ratio: ratio of hits out of total requests
  Hit ratios of 90% are common.
Problem: synchronizing cache and memory
  Write through
  Write back

## Slide 53: Step-by-Step Use of Cache: Hit

## Slide 54: Step-by-Step Use of Cache: Miss

## Slide 55: Performance Advantages
Hit ratios of 90% common
50%+ improved execution speed
Locality of reference is why caching works
  Most memory references confined to small region of memory at any given time
  Well-written program in small loop, procedure or function
  Data likely in array
  Variables stored together

## Slide 56: Multi-level Caches

## Slide 57: Cache vs. Virtual Memory
Cache speeds up memory access
Virtual memory increases amount of perceived storage
  independence from the configuration and capacity of the memory system
  low cost per bit

## Slide 58: Questions